## Slide 1: Hi-Landers Ham Class
Instructed by Rich Bugarin W6EC

## Slide 2: Sub-element 1 of 10

## Slide 3
Ham Radio Technician Class Exam preparation Power Point created by Rich Bugarin W6EC.
Effective July 1, 2022 and is valid until June 30, 2026.
Please send suggested changes to this presentation to:
w6ec@thebugarins.com

## Slide 4: Study Hints
I suggest you read each question and only the correct answer. Read through the complete question pool at least three times before you attempt taking a practice exams. For higher impact and better results read the correct answer first then the question and again the correct answer.
The key to passing the exam is to get the most questions correct using the above method the correct response will often jump out at you on test day even if you don’t remember the question.

## Slide 5: Text Color
Black: Original/Official questions and information in original format (unaltered).
Red: Original information text color simply changed to highlight subject.
Blue: Notes and information added by Rich (W6EC).

## Slide 6: 2022 Technician Class (FCC Element 2)
35 Exam questions

## Slide 7: 2018 Technician Class (Element 2)
There are 442 questions in this pool out of which you will have 35 on your Exam. The question pool is broken into subelements. Subelements are also subdivided into topic sections. You will have one question from each section on your official Exam.

## Slide 8: SUBELEMENT T1
FCC Rules, descriptions, and definitions for the Amateur Radio Service, operator and station license responsibilities
[6 Exam Questions - 6 Groups]

## Slide 9
T1A - Amateur Radio Service: purpose and permissible use of the Amateur Radio Service, operator/primary station license grant; Meanings of basic terms used in FCC rules; Interference; RACES rules; Phonetics; Frequency Coordinator
#1 of 35

## Slide 10: T1A01 [97.1]
Which of the following is a purpose of the Amateur Radio Service as stated in the FCC rules and regulations?
A. Providing personal radio communications for as many citizens as possible
B. Providing communications for international non-profit organizations
C. Advancing skills in the technical and communication phases of the radio art
D. All of these choices are correct

## Slide 11: T1A01 [97.1]
Which of the following is a purpose of the Amateur Radio Service as stated in the FCC rules and regulations?
A. Providing personal radio communications for as many citizens as possible
B. Providing communications for international non-profit organizations
C. Advancing skills in the technical and communication phases of the radio art
D. All of these choices are correct

## Slide 12: T1A02 [97.1]
What agency regulates and enforces the rules for the Amateur Radio Service in the United States?
A. FEMA
B. Homeland Security
C. The FCC
D. All these choices are correct

## Slide 13: T1A02 [97.1]
What agency regulates and enforces the rules for the Amateur Radio Service in the United States?
A. FEMA
B. Homeland Security
C. The FCC
D. All these choices are correct

## Slide 14: T1A03 [97.119(b)(2)]
What are the FCC rules regarding the use of a phonetic alphabet for station identification in the Amateur Radio Service?
A. It is required when transmitting emergency messages
B. It is encouraged
C. It is required when in contact with foreign stations
D. All these choices are correct

## Slide 15: T1A03 [97.119(b)(2)]
What are the FCC rules regarding the use of a phonetic alphabet for station identification in the Amateur Radio Service?
A. It is required when transmitting emergency messages
B. It is encouraged
C. It is required when in contact with foreign stations
D. All these choices are correct

## Slide 16: T1A04 [97.5(b)(1)]
How many operator/primary station license grants may be held by any one person?
A. One
B. No more than two
C. One for each band on which the person plans to operate
D. One for each permanent station location from which the person plans to operate

## Slide 17: T1A04 [97.5(b)(1)]
How many operator/primary station license grants may be held by any one person?
A. One
B. No more than two
C. One for each band on which the person plans to operate
D. One for each permanent station location from which the person plans to operate

## Slide 18: T1A05 [97.7]
What proves that the FCC has issued an operator/primary license grant?
A. A printed copy of the certificate of successful completion of examination
B. An email notification from the NCVEC granting the license
C. The license appears in the FCC ULS database
D. All these choices are correct

## Slide 19: T1A05 [97.7]
What proves that the FCC has issued an operator/primary license grant?
A. A printed copy of the certificate of successful completion of examination
B. An email notification from the NCVEC granting the license
C. The license appears in the FCC ULS database
D. All these choices are correct

## Slide 20: T1A06 [97.3(a)(9)]
What is the FCC Part 97 definition of a "beacon"?
A. A government transmitter marking the amateur radio band edges
B. A bulletin sent by the FCC to announce a national emergency
C. A continuous transmission of weather information authorized in the amateur bands by the National Weather Service
D. An amateur station transmitting communications for the purposes of observing propagation or related experimental activities

## Slide 21: T1A06 [97.3(a)(9)]
What is the FCC Part 97 definition of a "beacon"?
A. A government transmitter marking the amateur radio band edges
B. A bulletin sent by the FCC to announce a national emergency
C. A continuous transmission of weather information authorized in the amateur bands by the National Weather Service
D. An amateur station transmitting communications for the purposes of observing propagation or related experimental activities

## Slide 22: T1A07 [97.3(a)(41)]
What is the FCC Part 97 definition of a "space station"?
A. Any satellite orbiting the Earth
B. A manned satellite orbiting the Earth
C. An amateur station located more than 50 km above the Earth's surface
D. An amateur station using amateur radio satellites for relay of signals

## Slide 23: T1A07 [97.3(a)(41)]
What is the FCC Part 97 definition of a "space station"?
A. Any satellite orbiting the Earth
B. A manned satellite orbiting the Earth
C. An amateur station located more than 50 km above the Earth's surface
D. An amateur station using amateur radio satellites for relay of signals

## Slide 24: T1A08 [97.3(a)(22)]
Which of the following entities recommends transmit/receive channels and other parameters for auxiliary and repeater stations?
A. Frequency Spectrum Manager appointed by the FCC
B. Volunteer Frequency Coordinator recognized by local amateurs
C. FCC Regional Field Office
D. International Telecommunications Union

## Slide 25: T1A08 [97.3(a)(22)]
Which of the following entities recommends transmit/receive channels and other parameters for auxiliary and repeater stations?
A. Frequency Spectrum Manager appointed by the FCC
B. Volunteer Frequency Coordinator recognized by local amateurs
C. FCC Regional Field Office
D. International Telecommunications Union

## Slide 26: T1A09 [97.3(a)(22)]
Who selects a Frequency Coordinator?
A. The FCC Office of Spectrum Management and Coordination Policy
B. The local chapter of the Office of National Council of Independent Frequency Coordinators
C. Amateur operators in a local or regional area whose stations are eligible to be repeater or auxiliary stations
D. FCC Regional Field Office

## Slide 27: T1A09 [97.3(a)(22)]
Who selects a Frequency Coordinator?
A. The FCC Office of Spectrum Management and Coordination Policy
B. The local chapter of the Office of National Council of Independent Frequency Coordinators
C. Amateur operators in a local or regional area whose stations are eligible to be repeater or auxiliary stations
D. FCC Regional Field Office

## Slide 28: T1A10 [97.3(a)(38), 97.407]
What is the Radio Amateur Civil Emergency Service (RACES)?
A. A radio service using amateur frequencies for emergency management or civil defense communications
B. A radio service using amateur stations for emergency management or civil defense communications
C. An emergency service using amateur operators certified by a civil defense organization as being enrolled in that organization
D. All these choices are correct

## Slide 29: T1A10 [97.3(a)(38), 97.407]
What is the Radio Amateur Civil Emergency Service (RACES)?
A. A radio service using amateur frequencies for emergency management or civil defense communications
B. A radio service using amateur stations for emergency management or civil defense communications
C. An emergency service using amateur operators certified by a civil defense organization as being enrolled in that organization
D. All these choices are correct

## Slide 30: T1A11 [97.101 (d)]
When is willful interference to other amateur radio stations permitted?
A. To stop another amateur station that is breaking the FCC rules
B. At no time
C. When making short test transmissions
D. At any time, stations in the Amateur Radio Service are not protected from willful interference

## Slide 31: T1A11 [97.101 (d)]
When is willful interference to other amateur radio stations permitted?
A. To stop another amateur station that is breaking the FCC rules
B. At no time
C. When making short test transmissions
D. At any time, stations in the Amateur Radio Service are not protected from willful interference

## Slide 32
T1B - Authorized frequencies: frequency allocations; ITU; emission modes; restricted sub-bands; spectrum sharing; transmissions near band edges; contacting the International Space Station; power output
#2 of 35

## Slide 33: T1B01 [97.301 (e)]
Which of the following frequency ranges are available for phone operation by Technician licensees?
A. 28.050 MHz to 28.150 MHz
B. 28.100 MHz to 28.300 MHz
C. 28.300 MHz to 28.500 MHz
D. 28.500 MHz to 28.600 MHz

## Slide 34: T1B01 [97.301 (e)]
Which of the following frequency ranges are available for phone operation by Technician licensees?
A. 28.050 MHz to 28.150 MHz
B. 28.100 MHz to 28.300 MHz
C. 28.300 MHz to 28.500 MHz
D. 28.500 MHz to 28.600 MHz

## Slide 35: T1B02 [97.301, 97.207(c)]
Which amateurs may contact the International Space Station (ISS) on VHF bands?
A. Any amateur holding a General class or higher license
B. Any amateur holding a Technician class or higher license
C. Any amateur holding a General class or higher license who has applied for and received approval from NASA
D. Any amateur holding a Technician class or higher license who has applied for and received approval from NASA

## Slide 36: T1B02 [97.301, 97.207(c)]
Which amateurs may contact the International Space Station (ISS) on VHF bands?
A. Any amateur holding a General class or higher license
B. Any amateur holding a Technician class or higher license
C. Any amateur holding a General class or higher license who has applied for and received approval from NASA
D. Any amateur holding a Technician class or higher license who has applied for and received approval from NASA

## Slide 37: T1B03 [97.301(a)]
Which frequency is within the 6 meter band?
A. 49.00 MHz
B. 52.525 MHz
C. 28.50 MHz
D. 222.15 MHz

## Slide 38: T1B03 [97.301(a)]
Which frequency is within the 6 meter band?
A. 49.00 MHz
B. 52.525 MHz
C. 28.50 MHz
D. 222.15 MHz
Using Math
300 ÷ 6 (Meters) = 50 (MHz)
Logical answers must be close to this number 50. In this case it is the closest higher answer.
Observation often the correct Frequency ends in a “.525”

## Slide 39: T1B04 [97.301(a)]
Which amateur band includes 146.52 MHz?
A. 6 meters
B. 20 meters
C. 70 centimeters
D. 2 meters

## Slide 40: T1B04 [97.301(a)]
Which amateur band includes 146.52 MHz?
A. 6 meters
B. 20 meters
C. 70 centimeters
D. 2 meters
Math
300 ÷ 146.52 = 2.0475
Rounded off = 2 meters
But also note 146.525 is the 2 meter frequency the Hi-Landers use

## Slide 41: T1B05 [97.305(c)]
How may amateurs use the 219 to 220 MHz segment of 1.25 meter band?
A. Spread spectrum only
B. Fast-scan television only
C. Emergency traffic only
D. Fixed digital message forwarding systems only

## Slide 42: T1B05 [97.305(c)]
How may amateurs use the 219 to 220 MHz segment of 1.25 meter band?
A. Spread spectrum only
B. Fast-scan television only
C. Emergency traffic only
D. Fixed digital message forwarding systems only
See ARRL Technician Privileges hand out

## Slide 43: T1B06 [97.301(e), 97.305]
On which HF bands does a Technician class operator have phone privileges?
A. None
B. 10 meters only
C. 80 meters, 40 meters, 15 meters and 10 meters
D. 30 meters only

## Slide 44: T1B06 [97.301(e), 97.305]
On which HF bands does a Technician class operator have phone privileges?
A. None
B. 10 meters only
C. 80 meters, 40 meters, 15 meters and 10 meters
D. 30 meters only
HF = High Frequency
Long meters like 80, 40, 20, 10
Tech only has privileges on 10m

## Slide 45: T1B07 [97.305(a), (c)]
Which of the following VHF/UHF band segments are limited to CW only?
A. 50.0 MHz to 50.1 MHz and 144.0 MHz to 144.1 MHz
B. 219 MHz to 220 MHz and 420.0 MHz to 420.1 MHz
C. 902.0 MHz to 902.1 MHz
D. All these choices are correct

## Slide 46: T1B07 [97.305(a), (c)]
Which of the following VHF/UHF band segments are limited to CW only?
A. 50.0 MHz to 50.1 MHz and 144.0 MHz to 144.1 MHz
B. 219 MHz to 220 MHz and 420.0 MHz to 420.1 MHz
C. 902.0 MHz to 902.1 MHz
D. All these choices are correctv
Note two groups of frequencies with .0 to .1 both groups

## Slide 47: T1B08 [97.303]
How are US amateurs restricted in segments of bands where the Amateur Radio Service is secondary?
A. U.S. amateurs may find non-amateur stations in those segments, and must avoid interfering with them
B. U.S. amateurs must give foreign amateur stations priority in those segments
C. International communications are not permitted in those segments
D. Digital transmissions are not permitted in those segments

## Slide 48: T1B08 [97.303]
How are US amateurs restricted in segments of bands where the Amateur Radio Service is secondary?
A. U.S. amateurs may find non-amateur stations in those segments, and must avoid interfering with them
B. U.S. amateurs must give foreign amateur stations priority in those segments
C. International communications are not permitted in those segments
D. Digital transmissions are not permitted in those segments

## Slide 49: T1B09 [97.101(a), 97.301(a-e)]
Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
A. To allow for calibration error in the transmitter frequency display
B. So that modulation sidebands do not extend beyond the band edge
C. To allow for transmitter frequency drift
D. All of these choices are correct

## Slide 50: T1B09 [97.101(a), 97.301(a-e)]
Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
A. To allow for calibration error in the transmitter frequency display
B. So that modulation sidebands do not extend beyond the band edge
C. To allow for transmitter frequency drift
D. All of these choices are correct

## Slide 51: T1B10 [97.305(c)]
Where may SSB phone be used in amateur bands above 50 MHz?
A. Only in sub-bands allocated to General class or higher licensees
B. Only on repeaters
C. In at least some segment of all these bands
D. On any band if the power is limited to 25 watts

## Slide 52: T1B10 [97.305(c)]
Where may SSB phone be used in amateur bands above 50 MHz?
A. Only in sub-bands allocated to General class or higher licensees
B. Only on repeaters
C. In at least some segment of all these bands
D. On any band if the power is limited to 25 watts
See ARRL Technician Privileges hand out

## Slide 53: T1B11 [97.313]
What is the maximum peak envelope power output for Technician class operators in their HF band segments?
A. 200 watts
B. 100 watts
C. 50 watts
D. 10 watts

## Slide 54: T1B11 [97.313]
What is the maximum peak envelope power output for Technician class operators in their HF band segments?
A. 200 watts
B. 100 watts
C. 50 watts
D. 10 watts
See ARRL Technician Privileges hand out

## Slide 55: T1B12 [97.313(b)]
Except for some specific restrictions, what is the maximum peak envelope power output for Technician class operators using frequencies above 30 MHz?
A. 50 watts
B. 100 watts
C. 500 watt
D. 1500 watts

## Slide 56: T1B12 [97.313(b)]
Except for some specific restrictions, what is the maximum peak envelope power output for Technician class operators using frequencies above 30 MHz?
A. 50 watts
B. 100 watts
C. 500 watt
D. 1500 watts
The restriction referred to here is on the all HF bands as in the last question (T1B11)

## Slide 57
T1C - Licensing: classes, sequential and vanity call sign systems, places where the Amateur Radio Service is regulated by the FCC, name and address on FCC license database, term, renewal, grace period, maintaining mailing address; International communications
#3 of 35

## Slide 58: T1C01 [97.9(a), 97.17(a)]
For which license classes are new licenses currently available from the FCC?
A. Novice, Technician, General, Amateur Extra
B. Technician, Technician Plus, General, Amateur Extra
C. Novice, Technician Plus, General, Advanced
D. Technician, General, Amateur Extra

## Slide 59: T1C01 [97.9(a), 97.17(a)]
For which license classes are new licenses currently available from the FCC?
A. Novice, Technician, General, Amateur Extra
B. Technician, Technician Plus, General, Amateur Extra
C. Novice, Technician Plus, General, Advanced
D. Technician, General, Amateur Extra

## Slide 60: T1C02 [97.19]
Who may select a desired call sign under the vanity call sign rules?
A. Only a licensed amateur with a General or Amateur Extra class license
B. Only a licensed amateur with an Amateur Extra class license
C. Only a licensed amateur who has been licensed continuously for more than 10 years
D. Any licensed amateur

## Slide 61: T1C02 [97.19]
Who may select a desired call sign under the vanity call sign rules?
A. Only a licensed amateur with a General or Amateur Extra class license
B. Only a licensed amateur with an Amateur Extra class license
C. Only a licensed amateur who has been licensed continuously for more than 10 years
D. Any licensed amateur

## Slide 62: T1C03 [97.117]
What types of international communications are an FCC-licensed amateur radio station permitted to make?
A. Communications incidental to the purposes of the Amateur Radio Service and remarks of a personal character
B. Communications incidental to conducting business or remarks of a personal nature
C. Only communications incidental to contest exchanges; all other communications are prohibited
D. Any communications that would be permitted by an international broadcast station

## Slide 63: T1C03 [97.117]
What types of international communications are an FCC-licensed amateur radio station permitted to make?
A. Communications incidental to the purposes of the Amateur Radio Service and remarks of a personal character
B. Communications incidental to conducting business or remarks of a personal nature
C. Only communications incidental to contest exchanges; all other communications are prohibited
D. Any communications that would be permitted by an international broadcast station

## Slide 64: T1C04 [97.23]
What may happen if the FCC is unable to reach you by email?
A. Fine and suspension of operator license
B. Revocation of the station license or suspension of the operator license
C. Revocation of access to the license record in the FCC system
D. Nothing; there is no such requirement

## Slide 65: T1C04 [97.23]
What may happen if the FCC is unable to reach you by email?
A. Fine and suspension of operator license
B. Revocation of the station license or suspension of the operator license
C. Revocation of access to the license record in the FCC system
D. Nothing; there is no such requirement

## Slide 66: T1C05
Which of the following is a valid Technician class call sign format?
A. KF1XXX
B. KA1X
C. W1XX
D. All these choices are correct

## Slide 67: T1C05
Which of the following is a valid Technician class call sign format?
A. KF1XXX
B. KA1X
C. W1XX
D. All these choices are correct
This is a 2 x 3 Call sign. A two letter prefix, a single zone number, followed by a 3 letter suffix.
US Calls start with an A K N and W

## Slide 68: T1C06 [97.5(a)(2)]
From which of the following locations may an FCC-licensed amateur station transmit?
A. From within any country that belongs to the International Telecommunications Union
B. From within any country that is a member of the United Nations
C. From anywhere within International Telecommunication Union (ITU) Regions 2 and 3
D. From any vessel or craft located in international waters and documented or registered in the United States

## Slide 69: T1C06 [97.5(a)(2)]
From which of the following locations may an FCC-licensed amateur station transmit?
A. From within any country that belongs to the International Telecommunications Union
B. From within any country that is a member of the United Nations
C. From anywhere within International Telecommunication Union (ITU) Regions 2 and 3
D. From any vessel or craft located in international waters and documented or registered in the United States

## Slide 70: T1C07 [97.23]
Which of the following can result in revocation of the station license or suspension of the operator license?
A. Failure to inform the FCC of any changes in the amateur station following performance of an RF safety environmental evaluation
B. Failure to provide and maintain a correct email address with the FCC
C. Failure to obtain FCC type acceptance prior to using a home-built transmitter
D. Failure to have a copy of your license available at your station

## Slide 71: T1C07 [97.23]
Which of the following can result in revocation of the station license or suspension of the operator license?
A. Failure to inform the FCC of any changes in the amateur station following performance of an RF safety environmental evaluation
B. Failure to provide and maintain a correct email address with the FCC
C. Failure to obtain FCC type acceptance prior to using a home-built transmitter
D. Failure to have a copy of your license available at your station

## Slide 72: T1C08 [97.25]
What is the normal term for an FCC-issued amateur radio license?
A. Five years
B. Life
C. Ten years
D. Eight years

## Slide 73: T1C08 [97.25]
What is the normal term for an FCC-issued amateur radio license?
A. Five years
B. Life
C. Ten years
D. Eight years

## Slide 74: T1C09 [97.21(a)(b)]
What is the grace period for renewal if an amateur license expires?
A. Two years
B. Three years
C. Five years
D. Ten years

## Slide 75: T1C09 [97.21(a)(b)]
What is the grace period for renewal if an amateur license expires?
A. Two years
B. Three years
C. Five years
D. Ten years

## Slide 76: T1C10 [97.5a]
How soon after passing the examination for your first amateur radio license may you transmit on the amateur radio bands?
A. Immediately on receiving your Certificate of Successful Completion of Examination (CSCE)
B. As soon as your operator/station license grant appears on the ARRL website
C. As soon as your operator/station license grant appears in the FCC’s license database
D. As soon as you receive your license in the mail from the FCC

## Slide 77: T1C10 [97.5a]
How soon after passing the examination for your first amateur radio license may you transmit on the amateur radio bands?
A. Immediately on receiving your Certificate of Successful Completion of Examination (CSCE)
B. As soon as your operator/station license grant appears on the ARRL website
C. As soon as your operator/station license grant appears in the FCC’s license database
D. As soon as you receive your license in the mail from the FCC

## Slide 78: T1C11 [97.21(b)]
If your license has expired and is still within the allowable grace period, may you continue to transmit on the amateur radio bands?
A. Yes, for up to two years
B. Yes, as soon as you apply for renewal
C. Yes, for up to one year
D. No, you must wait until the license has been renewed

## Slide 79: T1C11 [97.21(b)]
If your license has expired and is still within the allowable grace period, may you continue to transmit on the amateur radio bands?
A. Yes, for up to two years
B. Yes, as soon as you apply for renewal
C. Yes, for up to one year
D. No, you must wait until the license has been renewed

## Slide 80
T1D - Authorized and prohibited transmissions: communications with other countries, music, exchange of information with other services, indecent language, compensation for operating, retransmission of other amateur signals, encryption, sale of equipment, unidentified transmissions, one-way transmission
#4 of 35

## Slide 81: T1D01 [97.111(a)(1)]
With which countries are FCC-licensed amateur radio stations prohibited from exchanging communications?
A. Any country whose administration has notified the International Telecommunication Union (ITU) that it objects to such communications
B. Any country whose administration has notified the American Radio Relay League (ARRL) that it objects to such communications
C. Any country banned from such communications by the International Amateur Radio Union (IARU)
D. Any country banned from making such communications by the American Radio Relay League (ARRL)

## Slide 82: T1D01 [97.111(a)(1)]
With which countries are FCC-licensed amateur radio stations prohibited from exchanging communications?
A. Any country whose administration has notified the International Telecommunication Union (ITU) that it objects to such communications
B. Any country whose administration has notified the American Radio Relay League (ARRL) that it objects to such communications
C. Any country banned from such communications by the International Amateur Radio Union (IARU)
D. Any country banned from making such communications by the American Radio Relay League (ARRL)

## Slide 83: T1D02 [97.113(b), 97.111(b)]
Under which of the following circumstances are one-way transmissions by an amateur station prohibited?
A. In all circumstances
B. Broadcasting
C. International Morse Code Practice
D. Telecommand or transmissions of telemetry

## Slide 84: T1D02 [97.113(b), 97.111(b)]
Under which of the following circumstances are one-way transmissions by an amateur station prohibited?
A. In all circumstances
B. Broadcasting
C. International Morse Code Practice
D. Telecommand or transmissions of telemetry

## Slide 85: T1D03 [97.211(b), 97.215(b), 97.113(a)(4)]
When is it permissible to transmit messages encoded to obscure their meaning?
A. Only during contests
B. Only when transmitting certain approved digital codes
C. Only when transmitting control commands to space stations or radio control craft
D. Never

## Slide 86: T1D03 [97.211(b), 97.215(b), 97.113(a)(4)]
When is it permissible to transmit messages encoded to obscure their meaning?
A. Only during contests
B. Only when transmitting certain approved digital codes
C. Only when transmitting control commands to space stations or radio control craft
D. Never

## Slide 87: T1D04 [97.113(a)(4), 97.113(c)]
Under what conditions is an amateur station authorized to transmit music using a phone emission?
A. When incidental to an authorized retransmission of manned spacecraft communications
B. When the music produces no spurious emissions
C. When transmissions are limited to less than three minutes per hour
D. When the music is transmitted above 1280 MHz

## Slide 88: T1D04 [97.113(a)(4), 97.113(c)]
Under what conditions is an amateur station authorized to transmit music using a phone emission?
A. When incidental to an authorized retransmission of manned spacecraft communications
B. When the music produces no spurious emissions
C. When transmissions are limited to less than three minutes per hour
D. When the music is transmitted above 1280 MHz

## Slide 89: T1D05 [97.113(a)(3)(ii)]
When may amateur radio operators use their stations to notify other amateurs of the availability of equipment for sale or trade?
A. Never
B. When the equipment is not the personal property of either the station licensee, or the control operator, or their close relatives
C. When no profit is made on the sale
D. When selling amateur radio equipment and not on a regular basis

## Slide 90: T1D05 [97.113(a)(3)(ii)]
When may amateur radio operators use their stations to notify other amateurs of the availability of equipment for sale or trade?
A. Never
B. When the equipment is not the personal property of either the station licensee, or the control operator, or their close relatives
C. When no profit is made on the sale
D. When selling amateur radio equipment and not on a regular basis

## Slide 91: T1D06 [97.113(a)(4)]
What, if any, are the restrictions concerning transmission of language that may be considered indecent or obscene?
A. The FCC maintains a list of words that are not permitted to be used on amateur frequencies
B. Any such language is prohibited
C. The ITU maintains a list of words that are not permitted to be used on amateur frequencies
D. There is no such prohibition

## Slide 92: T1D06 [97.113(a)(4)]
What, if any, are the restrictions concerning transmission of language that may be considered indecent or obscene?
A. The FCC maintains a list of words that are not permitted to be used on amateur frequencies
B. Any such language is prohibited
C. The ITU maintains a list of words that are not permitted to be used on amateur frequencies
D. There is no such prohibition

## Slide 93: T1D07 [97.113(d)]
What types of amateur stations can automatically retransmit the signals of other amateur stations?
A. Auxiliary, beacon, or Earth stations
B. Earth, repeater, or space stations
C. Beacon, repeater, or space stations
D. Repeater, auxiliary, or space stations

## Slide 94: T1D07 [97.113(d)]
What types of amateur stations can automatically retransmit the signals of other amateur stations?
A. Auxiliary, beacon, or Earth stations
B. Earth, repeater, or space stations
C. Beacon, repeater, or space stations
D. Repeater, auxiliary, or space stations

## Slide 95: T1D08 [97.113(a)(3)(iii)]
In which of the following circumstances may the control operator of an amateur station receive compensation for operating that station?
A. When the communication is related to the sale of amateur equipment by the control operator's employer
B. When the communication is incidental to classroom instruction at an educational institution
C. When the communication is made to obtain emergency information for a local broadcast station
D. All of these choices are correct

## Slide 96: T1D08 [97.113(a)(3)(iii)]
In which of the following circumstances may the control operator of an amateur station receive compensation for operating that station?
A. When the communication is related to the sale of amateur equipment by the control operator's employer
B. When the communication is incidental to classroom instruction at an educational institution
C. When the communication is made to obtain emergency information for a local broadcast station
D. All of these choices are correct

## Slide 97: T1D09 [97.113(5)(b)]
When may amateur stations transmit information in support of broadcasting, program production, or news gathering, assuming no other means is available?
A. When such communications are directly related to the immediate safety of human life or protection of property
B. When broadcasting communications to or from the space shuttle
C. Where noncommercial programming is gathered and supplied exclusively to the National Public Radio network
D. Never

## Slide 98: T1D09 [97.113(5)(b)]
When may amateur stations transmit information in support of broadcasting, program production, or news gathering, assuming no other means is available?
A. When such communications are directly related to the immediate safety of human life or protection of property
B. When broadcasting communications to or from the space shuttle
C. Where noncommercial programming is gathered and supplied exclusively to the National Public Radio network
D. Never
Transmitting to the general public is called broadcasting. Ham radios are Radio Telephones not licensed for broadcast except in an emergency.

## Slide 99: T1D10 [97.3(a)(10)]
How does the FCC define broadcasting for the Amateur Radio Service?
A. Two-way transmissions by amateur stations
B. Any transmission made by the licensed station
C. Transmission of messages directed only to amateur operators
D. Transmissions intended for reception by the general public

## Slide 100: T1D10 [97.3(a)(10)]
How does the FCC define broadcasting for the Amateur Radio Service?
A. Two-way transmissions by amateur stations
B. Any transmission made by the licensed station
C. Transmission of messages directed only to amateur operators
D. Transmissions intended for reception by the general public

## Slide 101: T1D11 [97.119(a)]
When may an amateur station transmit without identifying on the air?
A. When the transmissions are of a brief nature to make station adjustments
B. When the transmissions are unmodulated
C. When the transmitted power level is below 1 watt
D. When transmitting signals to control model craft

## Slide 102: T1D11 [97.119(a)]
When may an amateur station transmit without identifying on the air?
A. When the transmissions are of a brief nature to make station adjustments
B. When the transmissions are unmodulated
C. When the transmitted power level is below 1 watt
D. When transmitting signals to control model craft

## Slide 103
T1E - Control operator: eligibility, designating, privileges, duties, location, required; Control point; Control types: automatic, remote
#5 of 35

## Slide 104: T1E01 [97.7(a)]
When may an amateur station transmit without a control operator?
A. When using automatic control, such as in the case of a repeater
B. When the station licensee is away and another licensed amateur is using the station
C. When the transmitting station is an auxiliary station
D. Never

## Slide 105: T1E01 [97.7(a)]
When may an amateur station transmit without a control operator?
A. When using automatic control, such as in the case of a repeater
B. When the station licensee is away and another licensed amateur is using the station
C. When the transmitting station is an auxiliary station
D. Never

## Slide 106: T1E02 [97.301, 97.207(c)]
Who may be the control operator of a station communicating through an amateur satellite or space station?
A. Only an Amateur Extra class operator
B. A General class or higher licensee who has a satellite operator certification
C. Only an Amateur Extra class operator who is also an AMSAT member
D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency

## Slide 107: T1E02 [97.301, 97.207(c)]
Who may be the control operator of a station communicating through an amateur satellite or space station?
A. Only an Amateur Extra class operator
B. A General class or higher licensee who has a satellite operator certification
C. Only an Amateur Extra class operator who is also an AMSAT member
D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency

## Slide 108: T1E03 [97.103(b)]
Who must designate the station control operator?
A. The station licensee
B. The FCC
C. The frequency coordinator
D. Any licensed operator

## Slide 109: T1E03 [97.103(b)]
Who must designate the station control operator?
A. The station licensee
B. The FCC
C. The frequency coordinator
D. Any licensed operator

## Slide 110: T1E04 [97.103(b)]
What determines the transmitting privileges of an amateur station?
A. The frequency authorized by the frequency coordinator
B. The frequencies printed on the license grant
C. The highest class of operator license held by anyone on the premises
D. The class of operator license held by the control operator

## Slide 111: T1E04 [97.103(b)]
What determines the transmitting privileges of an amateur station?
A. The frequency authorized by the frequency coordinator
B. The frequencies printed on the license grant
C. The highest class of operator license held by anyone on the premises
D. The class of operator license held by the control operator

## Slide 112: T1E05 [97.3(a)(14)]
What is an amateur station control point?
A. The location of the station’s transmitting antenna
B. The location of the station transmitting apparatus
C. The location at which the control operator function is performed
D. The mailing address of the station licensee

## Slide 113: T1E05 [97.3(a)(14)]
What is an amateur station control point?
A. The location of the station’s transmitting antenna
B. The location of the station transmitting apparatus
C. The location at which the control operator function is performed
D. The mailing address of the station licensee

## Slide 114: T1E06 [97.301]
When, under normal circumstances, may a Technician class licensee be the control operator of a station operating in an Amateur Extra Class band segment?
A. At no time
B. When designated as the control operator by an Amateur Extra Class licensee
C. As part of a multi-operator contest team
D. When using a club station whose trustee holds an Amateur Extra Class license

## Slide 115: T1E06 [97.301]
When, under normal circumstances, may a Technician class licensee be the control operator of a station operating in an Amateur Extra Class band segment?
A. At no time
B. When designated as the control operator by an Amateur Extra Class licensee
C. As part of a multi-operator contest team
D. When using a club station whose trustee holds an Amateur Extra Class license

## Slide 116: T1E07 [97.103(a)]
When the control operator is not the station licensee, who is responsible for the proper operation of the station?
A. All licensed amateurs who are present at the operation
B. Only the station licensee
C. Only the control operator
D. The control operator and the station licensee
Notes: Combo

## Slide 117: T1E07 [97.103(a)]
When the control operator is not the station licensee, who is responsible for the proper operation of the station?
A. All licensed amateurs who are present at the operation
B. Only the station licensee
C. Only the control operator
D. The control operator and the station licensee
Notes: Combo

## Slide 118: T1E08 [97.3(a)(6), 97.205(d)]
Which of the following is an example of automatic control?
A. Repeater operation
B. Controlling the station over the Internet
C. Using a computer or other device to send CW automatically
D. Using a computer or other device to identify automatically

## Slide 119: T1E08 [97.3(a)(6), 97.205(d)]
Which of the following is an example of automatic control?
A. Repeater operation
B. Controlling the station over the Internet
C. Using a computer or other device to send CW automatically
D. Using a computer or other device to identify automatically

## Slide 120: T1E09 [97.109(c)]
Which of the following are required for remote control operation?
A. The control operator must be at the control point
B. A control operator is required at all times
C. The control operator must indirectly manipulate the controls
D. All these choices are correct

## Slide 121: T1E09 [97.109(c)]
Which of the following are required for remote control operation?
A. The control operator must be at the control point
B. A control operator is required at all times
C. The control operator must indirectly manipulate the controls
D. All these choices are correct

## Slide 122: T1E10 [97.3(a)(39)]
Which of the following is an example of remote control as defined in Part 97?
A. Repeater operation
B. Operating the station over the Internet
C. Controlling a model aircraft, boat or car by amateur radio
D. All of these choices are correct

## Slide 123: T1E10 [97.3(a)(39)]
Which of the following is an example of remote control as defined in Part 97?
A. Repeater operation
B. Operating the station over the Internet
C. Controlling a model aircraft, boat or car by amateur radio
D. All of these choices are correct
Remote control for this question is referring to remotely tuning and operating a radio transmitter.

## Slide 124: T1E11 [97.103(a)]
Who does the FCC presume to be the control operator of an amateur station, unless documentation to the contrary is in the station records?
A. The station custodian
B. The third party participant
C. The person operating the station equipment
D. The station licensee

## Slide 125: T1E11 [97.103(a)]
Who does the FCC presume to be the control operator of an amateur station, unless documentation to the contrary is in the station records?
A. The station custodian
B. The third party participant
C. The person operating the station equipment
D. The station licensee

## Slide 126
T1F - Station identification; repeaters; third-party communications; club stations; FCC inspection
#6 of 35

## Slide 127: T1F01 [97.103(c)]
When must the station and its records be available for FCC inspection?
A. At any time ten days after notification by the FCC of such an inspection
B. At any time upon request by an FCC representative
C. At any time after written notification by the FCC of such inspection
D. Only when presented with a valid warrant by an FCC official or government agent

## Slide 128: T1F01 [97.103(c)]
When must the station and its records be available for FCC inspection?
A. At any time ten days after notification by the FCC of such an inspection
B. At any time upon request by an FCC representative
C. At any time after written notification by the FCC of such inspection
D. Only when presented with a valid warrant by an FCC official or government agent

## Slide 129: T1F02 [97.119 (a)]
How often must you identify with your FCC-assigned call sign when using tactical call signs such as “Race Headquarters”?
A. Never, the tactical call is sufficient
B. Once during every hour
C. At the end of each communication and every ten minutes during a communication
D. At the end of every transmission

## Slide 130: T1F02 [97.119 (a)]
How often must you identify with your FCC-assigned call sign when using tactical call signs such as “Race Headquarters”?
A. Never, the tactical call is sufficient
B. Once during every hour
C. At the end of each communication and every ten minutes during a communication
D. At the end of every transmission

## Slide 131: T1F03 [97.119(a)]
When are you required to transmit your assigned call sign?
A. At the beginning of each contact, and every 10 minutes thereafter
B. At least once during each transmission
C. At least every 15 minutes during and at the end of a communication
D. At least every 10 minutes during and at the end of a communication

## Slide 132: T1F03 [97.119(a)]
When are you required to transmit your assigned call sign?
A. At the beginning of each contact, and every 10 minutes thereafter
B. At least once during each transmission
C. At least every 15 minutes during and at the end of a communication
D. At least every 10 minutes during and at the end of a communication

## Slide 133: T1F04 [97.119(b) (2)]
Which of the following is an acceptable language for use for station identification when operating in a phone sub-band?
Any language recognized by the United Nations
Any language recognized by the ITU
English
English, French, or Spanish

## Slide 134: T1F04 [97.119(b) (2)]
What language may you use for identification when operating in a phone sub-band?
A. Any language recognized by the United Nations
B. Any language recognized by the ITU
C. English
D. English, French, or Spanish

## Slide 135: T1F05 [97.119(b)(2)]
What method of call sign identification is required for a station transmitting phone signals?
A. Send the call sign followed by the indicator RPT
B. Send the call sign using CW or phone emission
C. Send the call sign followed by the indicator R
D. Send the call sign using only phone emission

## Slide 136: T1F05 [97.119(b)(2)]
What method of call sign identification is required for a station transmitting phone signals?
A. Send the call sign followed by the indicator RPT
B. Send the call sign using CW or phone emission
C. Send the call sign followed by the indicator R
D. Send the call sign using only phone emission
CW is Mores Code you may ID by verbally saying your call or by Mores Code

## Slide 137: T1F06 [97.119(c)]
Which of the following self-assigned indicators are acceptable when using a phone transmission?
A. KL7CC stroke W3
B. KL7CC slant W3
C. KL7CC slash W3
D. All these choices are correct

## Slide 138: T1F06 [97.119(c)]
Which of the following self-assigned indicators are acceptable when using a phone transmission?
A. KL7CC stroke W3
B. KL7CC slant W3
C. KL7CC slash W3
D. All these choices are correct

## Slide 139: T1F07 [97.115(a)(2)]
Which of the following restrictions apply when a non-licensed person is allowed to speak to a foreign station using a station under the control of a licensed amateur operator?
A. The person must be a U.S. citizen
B. The foreign station must be in a country with which the U.S. has a third party agreement
C. The licensed control operator must do the station identification
D. All these choices are correct

## Slide 140: T1F07 [97.115(a)(2)]
Which of the following restrictions apply when a non-licensed person is allowed to speak to a foreign station using a station under the control of a licensed amateur operator?
A. The person must be a U.S. citizen
B. The foreign station must be in a country with which the U.S. has a third party agreement
C. The licensed control operator must do the station identification
D. All these choices are correct

## Slide 141: T1F08 [97.3(a)(47)]
What is the definition of third party communications?
A. A message from a control operator to another amateur station control operator on behalf of another person
B. Amateur radio communications where three stations are in communications with one another
C. Operation when the transmitting equipment is licensed to a person other than the control operator
D. Temporary authorization for an unlicensed person to transmit on the amateur bands for technical experiments
Notes: Never

## Slide 142: T1F08 [97.3(a)(47)]
What is the definition of third party communications?
A. A message from a control operator to another amateur station control operator on behalf of another person
B. Amateur radio communications where three stations are in communications with one another
C. Operation when the transmitting equipment is licensed to a person other than the control operator
D. Temporary authorization for an unlicensed person to transmit on the amateur bands for technical experiments
Notes: Never

## Slide 143: T1F09 [97.3(a)(40)]
What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
A. Beacon station
B. Earth station
C. Repeater station
D. Message forwarding station

## Slide 144: T1F09 [97.3(a)(40)]
What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
A. Beacon station
B. Earth station
C. Repeater station
D. Message forwarding station

## Slide 145: T1F10 [97.205(g)]
Who is accountable if a repeater inadvertently retransmits communications that violate the FCC rules?
A. The control operator of the originating station
B. The control operator of the repeater
C. The owner of the repeater
D. Both the originating station and the repeater owner

## Slide 146: T1F10 [97.205(g)]
Who is accountable if a repeater inadvertently retransmits communications that violate the FCC rules?
A. The control operator of the originating station
B. The control operator of the repeater
C. The owner of the repeater
D. Both the originating station and the repeater owner

## Slide 147: T1F11 [97.5(b)(2)]
Which of the following is a requirement for the issuance of a club station license grant?
A. The trustee must have an Amateur Extra class operator license grant
B. The club must have at least four members
C. The club must be registered with the American Radio Relay League
D. All of these choices are correct

## Slide 148: T1F11 [97.5(b)(2)]
Which of the following is a requirement for the issuance of a club station license grant?
A. The trustee must have an Amateur Extra class operator license grant
B. The club must have at least four members
C. The club must be registered with the American Radio Relay League
D. All of these choices are correct

## Slide 149
End of Sub-element 1
(17% completed)
Proceed to Sub-element 2 when ready