## Slide 1: Hi-Landers Ham Class
Instructed by Rich Bugarin W6EC

## Slide 2: Sub-element 2 of 10

## Slide 3
Ham Radio Technician Class Exam preparation Power Point created by Rich Bugarin W6EC.
Effective July 1, 2022 and is valid until June 30, 2026.
Please send suggested changes to this presentation to:
w6ec@thebugarins.com

## Slide 4: Study Hints
I suggest you read each question and only the correct answer. Read through the complete question pool at least three times before you attempt taking a practice exams. For higher impact and better results read the correct answer first then the question and again the correct answer.
The key to passing the exam is to get the most questions correct using the above method the correct response will often jump out at you on test day even if you don’t remember the question.

## Slide 5: Text Color
Black: Original/Official questions and information in original format (unaltered).
Red: Original information text color simply changed to highlight subject.
Blue: Notes and information added by Rich (W6EC).

## Slide 6
SUBELEMENT T2 - Operating Procedures
[3 Exam Questions - 3 Groups]

## Slide 7
T2A - Station operation: choosing an operating frequency, calling another station, test transmissions; Band plans: calling frequencies, repeater offsets
#7 of 35

## Slide 8: T2A01
What is a common repeater frequency offset in the 2 meter band?
A. Plus or minus 5 MHz
B. Plus or minus 600 kHz
C. Plus or minus 500 kHz
D. Plus or minus 1 MHz

## Slide 9: T2A01
What is a common repeater frequency offset in the 2 meter band?
A. Plus or minus 5 MHz
B. Plus or minus 600 kHz
C. Plus or minus 500 kHz
D. Plus or minus 1 MHz

## Slide 10: T2A02
What is the national calling frequency for FM simplex operations in the 2 meter band?
A. 146.520 MHz
B. 145.000 MHz
C. 432.100 MHz
D. 446.000 MHz

## Slide 11: T2A02
What is the national calling frequency for FM simplex operations in the 2 meter band?
A. 146.520 MHz
B. 145.000 MHz
C. 432.100 MHz
D. 446.000 MHz

## Slide 12: T2A03
What is a common repeater frequency offset in the 70 cm band?
A. Plus or minus 5 MHz
B. Plus or minus 600 kHz
C. Plus or minus 500 kHz
D. Plus or minus 1 MHz

## Slide 13: T2A03
What is a common repeater frequency offset in the 70 cm band?
A. Plus or minus 5 MHz
B. Plus or minus 600 kHz
C. Plus or minus 500 kHz
D. Plus or minus 1 MHz

## Slide 14: T2A04
What is an appropriate way to call another station on a repeater if you know the other station's call sign?
A. Say "break, break," then say the station's call sign
B. Say the station's call sign, then identify with your call sign
C. Say "CQ" three times, then the other station's call sign
D. Wait for the station to call CQ, then answer

## Slide 15: T2A04
What is an appropriate way to call another station on a repeater if you know the other station's call sign?
A. Say "break, break," then say the station's call sign
B. Say the station's call sign, then identify with your call sign
C. Say "CQ" three times, then the other station's call sign
D. Wait for the station to call CQ, then answer

## Slide 16: T2A05
How should you respond to a station calling CQ?
A. Transmit "CQ" followed by the other station’s call sign
B. Transmit your call sign followed by the other station’s call sign
C. Transmit the other station’s call sign followed by your call sign
D. Transmit a signal report followed by your call sign

## Slide 17: T2A05
How should you respond to a station calling CQ?
A. Transmit "CQ" followed by the other station’s call sign
B. Transmit your call sign followed by the other station’s call sign
C. Transmit the other station’s call sign followed by your call sign
D. Transmit a signal report followed by your call sign

## Slide 18: T2A06
Which of the following is required when making on-the-air test transmissions?
A. Identify the transmitting station
B. Conduct tests only between 10 p.m. and 6 a.m. local time
C. Notify the FCC of the transmissions
D. All these choices are correct

## Slide 19: T2A06
Which of the following is required when making on-the-air test transmissions?
A. Identify the transmitting station
B. Conduct tests only between 10 p.m. and 6 a.m. local time
C. Notify the FCC of the transmissions
D. All these choices are correct

## Slide 20: T2A07
What is meant by "repeater offset”?
A. The difference between a repeater’s transmit and receive frequencies
B. The repeater has a time delay to prevent interference
C. The repeater station identification is done on a separate frequency
D. The number of simultaneous transmit frequencies used by a repeater

## Slide 21: T2A07
What is meant by "repeater offset”?
A. The difference between a repeater’s transmit and receive frequencies
B. The repeater has a time delay to prevent interference
C. The repeater station identification is done on a separate frequency
D. The number of simultaneous transmit frequencies used by a repeater

## Slide 22: T2A08
What is the meaning of the procedural signal “CQ”?
A. Call on the quarter hour
B. Test transmission, no reply expected
C. Only the called station should transmit
D. Calling any station

## Slide 23: T2A08
What is the meaning of the procedural signal “CQ”?
A. Call on the quarter hour
B. Test transmission, no reply expected
C. Only the called station should transmit
D. Calling any station

## Slide 24: T2A09
Which of the following indicates that a station is listening on a repeater and looking for a contact?
A. “CQ CQ” followed by the repeater’s call sign
B. The station’s call sign followed by the word “monitoring”
C. The repeater call sign followed by the station’s call sign
D. “QSY” followed by your call sign

## Slide 25: T2A09
Which of the following indicates that a station is listening on a repeater and looking for a contact?
A. “CQ CQ” followed by the repeater’s call sign
B. The station’s call sign followed by the word “monitoring”
C. The repeater call sign followed by the station’s call sign
D. “QSY” followed by your call sign

## Slide 26: T2A10
What is a band plan, beyond the privileges established by the FCC?
A. A voluntary guideline for using different modes or activities within an amateur band
B. A list of operating schedules
C. A list of available net frequencies
D. A plan devised by a club to indicate frequency band usage

## Slide 27: T2A10
What is a band plan, beyond the privileges established by the FCC?
A. A voluntary guideline for using different modes or activities within an amateur band
B. A list of operating schedules
C. A list of available net frequencies
D. A plan devised by a club to indicate frequency band usage

## Slide 28: T2A11
What term describes an amateur station that is transmitting and receiving on the same frequency?
A. Full duplex
B. Diplex
C. Simplex
D. Multiplex

## Slide 29: T2A11
What term describes an amateur station that is transmitting and receiving on the same frequency?
A. Full duplex
B. Diplex
C. Simplex
D. Multiplex

## Slide 30: T2A12
What should you do before calling CQ?
A. Listen first to be sure that no one else is using the frequency
B. Ask if the frequency is in use
C. Make sure you are authorized to use that frequency
D. All these choices are correct

## Slide 31: T2A12
What should you do before calling CQ?
A. Listen first to be sure that no one else is using the frequency
B. Ask if the frequency is in use
C. Make sure you are authorized to use that frequency
D. All these choices are correct

## Slide 32
T2B – VHF/UHF operating practices: FM repeater, simplex, reverse splits; Access tones: CTCSS, DTMF; DMR operation; Resolving operational problems; Q signals
#8 of 35

## Slide 33: T2B01
How is a VHF/UHF transceiver’s “reverse” function used?
A. To reduce power output
B. To increase power output
C. To listen on a repeater’s input frequency
D. To listen on a repeater’s output frequency

## Slide 34: T2B01
How is a VHF/UHF transceiver’s “reverse” function used?
A. To reduce power output
B. To increase power output
C. To listen on a repeater’s input frequency
D. To listen on a repeater’s output frequency

## Slide 35: T2B02
What term describes the use of a sub-audible tone transmitted along with normal voice audio to open the squelch of a receiver?
A. Carrier squelch
B. Tone burst
C. DTMF
D. CTCSS

## Slide 36: T2B02
What term describes the use of a sub-audible tone transmitted along with normal voice audio to open the squelch of a receiver?
A. Carrier squelch
B. Tone burst
C. DTMF
D. CTCSS
Continues Tone Controlled Squelch System

## Slide 37: T2B03
Which of the following describes a linked repeater network?
A. A network of repeaters in which signals received by one repeater are transmitted by all the repeaters in the network
B. A single repeater with more than one receiver
C. Multiple repeaters with the same control operator
D. A system of repeaters linked by APRS

## Slide 38: T2B03
Which of the following describes a linked repeater network?
A. A network of repeaters in which signals received by one repeater are transmitted by all the repeaters in the network
B. A single repeater with more than one receiver
C. Multiple repeaters with the same control operator
D. A system of repeaters linked by APRS

## Slide 39: T2B04
Which of the following could be the reason you are unable to access a repeater whose output you can hear?
A. Improper transceiver offset
B. You are using the wrong CTCSS tone
C. You are using the wrong DCS code
D. All these choices are correct

## Slide 40: T2B04
Which of the following could be the reason you are unable to access a repeater whose output you can hear?
A. Improper transceiver offset
B. You are using the wrong CTCSS tone
C. You are using the wrong DCS code
D. All these choices are correct

## Slide 41: T2B05
What would cause your FM transmission audio to be distorted on voice peaks?
A. Your repeater offset is inverted
B. You need to talk louder
C. You are talking too loudly
D. Your transmit power is too high

## Slide 42: T2B05
What would cause your FM transmission audio to be distorted on voice peaks?
A. Your repeater offset is inverted
B. You need to talk louder
C. You are talking too loudly
D. Your transmit power is too high

## Slide 43: T2B06
What type of signaling uses pairs of audio tones?
A. DTMF
B. CTCSS
C. GPRS
D. D-STAR

## Slide 44: T2B06
What type of signaling uses pairs of audio tones?
A. DTMF
B. CTCSS
C. GPRS
D. D-STAR
Duel Tone Multi Frequency (Proper name for Touch Tone Signals)
These tones are also used to control repeaters linked by the Internet Relay Linking Project (IRLP) protocol

## Slide 45: T2B07
How can you join a digital repeater’s “talkgroup”?
A. Register your radio with the local FCC office
B. Join the repeater owner’s club
C. Program your radio with the group’s ID or code
D. Sign your call after the courtesy tone

## Slide 46: T2B07
How can you join a digital repeater’s “talkgroup”?
A. Register your radio with the local FCC office
B. Join the repeater owner’s club
C. Program your radio with the group’s ID or code
D. Sign your call after the courtesy tone

## Slide 47: T2B08
Which of the following applies when two stations transmitting on the same frequency interfere with each other?
A. The stations should negotiate continued use of the frequency
B. Both stations should choose another frequency to avoid conflict
C. Interference is inevitable, so no action is required
D. Use subaudible tones so both stations can share the frequency

## Slide 48: T2B08
Which of the following applies when two stations transmitting on the same frequency interfere with each other?
A. The stations should negotiate continued use of the frequency
B. Both stations should choose another frequency to avoid conflict
C. Interference is inevitable, so no action is required
D. Use subaudible tones so both stations can share the frequency

## Slide 49: T2B09
Why are simplex channels designated in the VHF/UHF band plans?
A. So stations within range of each other can communicate without tying up a repeater
B. For contest operation
C. For working DX only
D. So stations with simple transmitters can access the repeater without automated offset

## Slide 50: T2B09
Why are simplex channels designated in the VHF/UHF band plans?
A. So stations within range of each other can communicate without tying up a repeater
B. For contest operation
C. For working DX only
D. So stations with simple transmitters can access the repeater without automated offset

## Slide 51: T2B10
Which Q signal indicates that you are receiving interference from other stations?
A. QRM
B. QRN
C. QTH
D. QSB

## Slide 52: T2B10
Which Q signal indicates that you are receiving interference from other stations?
A. QRM
B. QRN
C. QTH
D. QSB
Maybe “RM” = Receiving Mush

## Slide 53: T2B11
Which Q signal indicates that you are changing frequency?
A. QRU
B. QSY
C. QSL
D. QRZ

## Slide 54: T2B11
Which Q signal indicates that you are changing frequency?
A. QRU
B. QSY
C. QSL
D. QRZ
Maybe “SY” = Switching Frequency

## Slide 55: T2B12
What is the purpose of the color code used on DMR repeater systems?
A. Must match the repeater color code for access
B. Defines the frequency pair to use
C. Identifies the codec used
D. Defines the minimum signal level required for access

## Slide 56: T2B12
What is the purpose of the color code used on DMR repeater systems?
A. Must match the repeater color code for access
B. Defines the frequency pair to use
C. Identifies the codec used
D. Defines the minimum signal level required for access

## Slide 57: T2B13
What is the purpose of a squelch function?
A. Reduce a CW transmitter's key clicks
B. Mute the receiver audio when a signal is not present
C. Eliminate parasitic oscillations in an RF amplifier
D. Reduce interference from impulse noise

## Slide 58: T2B13
What is the purpose of a squelch function?
A. Reduce a CW transmitter's key clicks
B. Mute the receiver audio when a signal is not present
C. Eliminate parasitic oscillations in an RF amplifier
D. Reduce interference from impulse noise

## Slide 59
T2C – Public service: emergency operations, applicability of FCC rules, RACES and ARES, net and traffic procedures, operating restrictions during emergencies, use of phonetics in message handling
#9 of 35

## Slide 60: T2C01
When do FCC rules NOT apply to the operation of an amateur station?
A. When operating a RACES station
B. When operating under special FEMA rules
C. When operating under special ARES rules
D. FCC rules always apply

## Slide 61: T2C01
When do FCC rules NOT apply to the operation of an amateur station?
A. When operating a RACES station
B. When operating under special FEMA rules
C. When operating under special ARES rules
D. FCC rules always apply

## Slide 62: T2C02
Which of the following are typical duties of a Net Control Station?
A. Choose the regular net meeting time and frequency
B. Ensure that all stations checking into the net are properly licensed for operation on the net frequency
C. Call the net to order and direct communications between stations checking in
D. All these choices are correct

## Slide 63: T2C02
Which of the following are typical duties of a Net Control Station?
A. Choose the regular net meeting time and frequency
B. Ensure that all stations checking into the net are properly licensed for operation on the net frequency
C. Call the net to order and direct communications between stations checking in
D. All these choices are correct

## Slide 64: T2C03
What technique is used to ensure that voice messages containing unusual words are received correctly?
A. Send the words by voice and Morse code
B. Speak very loudly into the microphone
C. Spell the words using a standard phonetic alphabet
D. All these choices are correct

## Slide 65: T2C03
What technique is used to ensure that voice messages containing unusual words are received correctly?
A. Send the words by voice and Morse code
B. Speak very loudly into the microphone
C. Spell the words using a standard phonetic alphabet
D. All these choices are correct

## Slide 66: T2C04
What is RACES?
A. An emergency organization combining amateur radio and citizens band operators and frequencies
B. An international radio experimentation society
C. A radio contest held in a short period, sometimes called a “sprint”
D. An FCC part 97 amateur radio service for civil defense communications during national emergencies

## Slide 67: T2C04
What is RACES?
A. An emergency organization combining amateur radio and citizens band operators and frequencies
B. An international radio experimentation society
C. A radio contest held in a short period, sometimes called a “sprint”
D. An FCC part 97 amateur radio service for civil defense communications during national emergencies

## Slide 68: T2C05
What does the term “traffic” refer to in net operation?
A. Messages exchanged by net stations
B. The number of stations checking in and out of a net
C. Operation by mobile or portable stations
D. Requests to activate the net by a served agency

## Slide 69: T2C05
What does the term “traffic” refer to in net operation?
A. Messages exchanged by net stations
B. The number of stations checking in and out of a net
C. Operation by mobile or portable stations
D. Requests to activate the net by a served agency

## Slide 70: T2C06
What is the Amateur Radio Emergency Service (ARES)?
A. A group of licensed amateurs who have voluntarily registered their qualifications and equipment for communications duty in the public service
B. A group of licensed amateurs who are members of the military and who voluntarily agreed to provide message handling services in the case of an emergency
C. A training program that provides licensing courses for those interested in obtaining an amateur license to use during emergencies
D. A training program that certifies amateur operators for membership in the Radio Amateur Civil Emergency Service

## Slide 71: T2C06
What is the Amateur Radio Emergency Service (ARES)?
A. A group of licensed amateurs who have voluntarily registered their qualifications and equipment for communications duty in the public service
B. A group of licensed amateurs who are members of the military and who voluntarily agreed to provide message handling services in the case of an emergency
C. A training program that provides licensing courses for those interested in obtaining an amateur license to use during emergencies
D. A training program that certifies amateur operators for membership in the Radio Amateur Civil Emergency Service

## Slide 72: T2C07
Which of the following is standard practice when you participate in a net?
A. When first responding to the net control station, transmit your call sign, name, and address as in the FCC database
B. Record the time of each of your transmissions
C. Unless you are reporting an emergency, transmit only when directed by the net control station
D. All these choices are correct

## Slide 73: T2C07
Which of the following is standard practice when you participate in a net?
A. When first responding to the net control station, transmit your call sign, name, and address as in the FCC database
B. Record the time of each of your transmissions
C. Unless you are reporting an emergency, transmit only when directed by the net control station
D. All these choices are correct

## Slide 74: T2C08
Which of the following is a characteristic of good traffic handling?
A. Passing messages exactly as received
B. Making decisions as to whether messages are worthy of relay or delivery
C. Ensuring that any newsworthy messages are relayed to the news media
D. All these choices are correct

## Slide 75: T2C08
Which of the following is a characteristic of good traffic handling?
A. Passing messages exactly as received
B. Making decisions as to whether messages are worthy of relay or delivery
C. Ensuring that any newsworthy messages are relayed to the news media
D. All these choices are correct

## Slide 76: T2C09
Are amateur station control operators ever permitted to operate outside the frequency privileges of their license class?
A. No
B. Yes, but only when part of a FEMA emergency plan
C. Yes, but only when part of a RACES emergency plan
D. Yes, but only in situations involving the immediate safety of human life or protection of property

## Slide 77: T2C09
Are amateur station control operators ever permitted to operate outside the frequency privileges of their license class?
A. No
B. Yes, but only when part of a FEMA emergency plan
C. Yes, but only when part of a RACES emergency plan
D. Yes, but only in situations involving the immediate safety of human life or protection of property

## Slide 78: T2C10
What information is contained in the preamble of a formal traffic message?
A. The email address of the originating station
B. The address of the intended recipient
C. The telephone number of the addressee
D. Information needed to track the message

## Slide 79: T2C10
What information is contained in the preamble of a formal traffic message?
A. The email address of the originating station
B. The address of the intended recipient
C. The telephone number of the addressee
D. Information needed to track the message

## Slide 80: T2C11
What is meant by “check” in a radiogram header?
A. The number of words or word equivalents in the text portion of the message
B. The call sign of the originating station
C. A list of stations that have relayed the message
D. A box on the message form that indicates that the message was received and/or relayed

## Slide 81: T2C11
What is meant by “check” in a radiogram header?
A. The number of words or word equivalents in the text portion of the message
B. The call sign of the originating station
C. A list of stations that have relayed the message
D. A box on the message form that indicates that the message was received and/or relayed

## Slide 82
End of Sub-element 2
(25% completed)
Proceed to Sub-element 3 when ready