## Slide 1: Hi-Landers Ham Class
Instructed by Rich Bugarin W6EC

## Slide 2: Sub-element 5 of 10

## Slide 3
Ham Radio Technician Class Exam preparation Power Point created by Rich Bugarin W6EC.
Effective July 1, 2022 and is valid until June 30, 2026.
Please send suggested changes to this presentation to:
w6ec@thebugarins.com

## Slide 4: Study Hints
I suggest you read each question and only the correct answer. Read through the complete question pool at least three times before you attempt taking a practice exams. For higher impact and better results read the correct answer first then the question and again the correct answer.
The key to passing the exam is to get the most questions correct using the above method the correct response will often jump out at you on test day even if you don’t remember the question.

## Slide 5: Text Color
Black: Original/Official questions and information in original format (unaltered).
Red: Original information text color simply changed to highlight subject.
Blue: Notes and information added by Rich (W6EC).

## Slide 6
SUBELEMENT T6 – ELECTRONIC AND ELECTRICAL COMPONENTS
[4 Exam Questions - 4 Groups]

## Slide 7
T6A - Fixed and variable resistors; Capacitors; Inductors; Fuses; Switches; Batteries
#19 of 35

## Slide 8: T6A01
What electrical component opposes the flow of current in a DC circuit?
A. Inductor
B. Resistor
C. Inverter
D. Transformer

## Slide 9: T6A01
What electrical component opposes the flow of current in a DC circuit?
A. Inductor
B. Resistor
C. Inverter
D. Transformer

## Slide 10: T6A02
What type of component is often used as an adjustable volume control?
A. Fixed resistor
B. Power resistor
C. Potentiometer
D. Transformer

## Slide 11: T6A02
What type of component is often used as an adjustable volume control?
A. Fixed resistor
B. Power resistor
C. Potentiometer
D. Transformer

## Slide 12: T6A03
What electrical parameter is controlled by a potentiometer?
A. Inductance
B. Resistance
C. Capacitance
D. Field strength

## Slide 13: T6A03
What electrical parameter is controlled by a potentiometer?
A. Inductance
B. Resistance
C. Capacitance
D. Field strength

## Slide 14: T6A04
What electrical component stores energy in an electric field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 15: T6A04
What electrical component stores energy in an electric field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 16: T6A05
What type of electrical component consists of conductive surfaces separated by an insulator?
A. Resistor
B. Potentiometer
C. Oscillator
D. Capacitor

## Slide 17: T6A05
What type of electrical component consists of conductive surfaces separated by an insulator?
A. Resistor
B. Potentiometer
C. Oscillator
D. Capacitor

## Slide 18: T6A06
What type of electrical component stores energy in a magnetic field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 19: T6A06
What type of electrical component stores energy in a magnetic field?
A. Varistor
B. Capacitor
C. Inductor
D. Diode

## Slide 20: T6A07
What electrical component is typically constructed as a coil of wire?
A. Switch
B. Capacitor
C. Diode
D. Inductor

## Slide 21: T6A07
What electrical component is typically constructed as a coil of wire?
A. Switch
B. Capacitor
C. Diode
D. Inductor

## Slide 22: T6A08
What is the function of an SPDT switch?
A. A single circuit is opened or closed
B. Two circuits are opened or closed
C. A single circuit is switched between one of two other circuits
D. Two circuits are each switched between one of two other circuits

## Slide 23: T6A08
What is the function of an SPDT switch?
A. A single circuit is opened or closed
B. Two circuits are opened or closed
C. A single circuit is switched between one of two other circuits
D. Two circuits are each switched between one of two other circuits

## Slide 24: T6A09
What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Thyratron
C. Varactor
D. All these choices are correct

## Slide 25: T6A09
What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Thyratron
C. Varactor
D. All these choices are correct

## Slide 26: T6A10
Which of the following battery chemistries is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid
D. All these choices are correct

## Slide 27: T6A10
Which of the following battery chemistries is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid
D. All these choices are correct

## Slide 28: T6A11
Which of the following battery chemistries is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion

## Slide 29: T6A11
Which of the following battery chemistries is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion

## Slide 30: T6A12
What type of switch is represented by component 3 in figure T-2?
A. Single-pole single-throw
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw

## Slide 31: T6A12
What type of switch is represented by component 3 in figure T-2?
A. Single-pole single-throw (switch)
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw

## Slide 32
T6B – Semiconductors: basic principles and applications of solid state devices, diodes and transistors
#20 of 35

## Slide 33: T6B01
Which is true about forward voltage drop in a diode?
A. It is lower in some diode types than in others
B. It is proportional to peak inverse voltage
C. It indicates that the diode is defective
D. It has no impact on the voltage delivered to the load

## Slide 34: T6B01
Which is true about forward voltage drop in a diode?
A. It is lower in some diode types than in others
B. It is proportional to peak inverse voltage
C. It indicates that the diode is defective
D. It has no impact on the voltage delivered to the load
Forward Voltage for a Silicon Diode is about 0.7V for Germanium it is about 0.3V

## Slide 35: T6B02
What electronic component allows current to flow in only one direction?
A. Resistor
B. Fuse
C. Diode
D. Driven element

## Slide 36: T6B02
What electronic component allows current to flow in only one direction?
A. Resistor
B. Fuse
C. Diode
D. Driven element
A Diode (AKA Rectifier) functions as an Electronic Check Valve.

## Slide 37: T6B03
Which of these components can be used as an electronic switch?
A. Varistor
B. Potentiometer
C. Transistor
D. Thermistor

## Slide 38: T6B03
Which of these components can be used as an electronic switch?
A. Varistor
B. Potentiometer
C. Transistor
D. Thermistor

## Slide 39: T6B04
Which of the following components can consist of three regions of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter

## Slide 40: T6B04
Which of the following components can consist of three regions of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter

## Slide 41: T6B05
What type of transistor has a gate, drain, and source?
A. Varistor
B. Field-effect
C. Tesla-effect
D. Bipolar junction

## Slide 42: T6B05
What type of transistor has a gate, drain, and source?
A. Varistor
B. Field-effect
C. Tesla-effect
D. Bipolar junction

## Slide 43: T6B06
How is the cathode lead of a semiconductor diode often marked on the package?
A. With the word "cathode"
B. With a stripe
C. With the letter C
D. With the letter K

## Slide 44: T6B06
How is the cathode lead of a semiconductor diode often marked on the package?
A. With the word "cathode"
B. With a stripe
C. With the letter C
D. With the letter K

## Slide 45: T6B07
What causes a light-emitting diode (LED) to emit light?
A. Forward current
B. Reverse current
C. Capacitively-coupled RF signal
D. Inductively-coupled RF signal

## Slide 46: T6B07
What causes a light-emitting diode (LED) to emit light?
A. Forward current
B. Reverse current
C. Capacitively-coupled RF signal
D. Inductively-coupled RF signal
Forward typically means Pass Current
Reverse typically means Block Current

## Slide 47: T6B08
What does the abbreviation FET stand for?
A. Frequency Emission Transmitter
B. Fast Electron Transistor
C. Free Electron Transmitter
D. Field Effect Transistor

## Slide 48: T6B08
What does the abbreviation FET stand for?
A. Frequency Emission Transmitter
B. Fast Electron Transistor
C. Free Electron Transmitter
D. Field Effect Transistor

## Slide 49: T6B09
What are the names for the electrodes of a diode?
A. Plus and minus
B. Source and drain
C. Anode and cathode
D. Gate and base

## Slide 50: T6B09
What are the names for the electrodes of a diode?
A. Plus and minus
B. Source and drain
C. Anode and cathode
D. Gate and base
Anode Cathode

## Slide 51: T6B10
Which of the following can provide power gain?
A. Transformer
B. Transistor
C. Reactor
D. Resistor

## Slide 52: T6B10
Which of the following can provide power gain?
A. Transformer
B. Transistor
C. Reactor
D. Resistor
Transistors are voltage controlled variable resistors typically wired as an Amplifier

## Slide 53: T6B11
What is the term that describes a device's ability to amplify a signal?
A. Gain
B. Forward resistance
C. Forward voltage drop
D. On resistance

## Slide 54: T6B11
What is the term that describes a device's ability to amplify a signal?
A. Gain
B. Forward resistance
C. Forward voltage drop
D. On resistance

## Slide 55: T6B12
What are the names of the electrodes of a bipolar junction transistor?
A. Signal, bias, power
B. Emitter, base, collector
C. Input, output, supply
D. Pole one, pole two, output

## Slide 56: T6B12
What are the names of the electrodes of a bipolar junction transistor?
A. Signal, bias, power
B. Emitter, base, collector
C. Input, output, supply
D. Pole one, pole two, output
Collector
Base
Emitter

## Slide 57
T6C - Circuit diagrams: use of schematics, basic structure; Schematic symbols of basic components
#21 of 35

## Slide 58: T6C01
What is the name of an electrical wiring diagram that uses standard component symbols?
A. Bill of materials
B. Connector pinout
C. Schematic
D. Flow chart

## Slide 59: T6C01
What is the name of an electrical wiring diagram that uses standard component symbols?
A. Bill of materials
B. Connector pinout
C. Schematic
D. Flow chart

## Slide 60: T6C02
What is component 1 in figure T-1?
A. Resistor
B. Transistor
C. Battery
D. Connector
Figure T1

## Slide 61: T6C02
What is component 1 in figure T-1?
A. Resistor
B. Transistor
C. Battery
D. Connector
Figure T1

## Slide 62: T6C03
What is component 2 in figure T-1?
A. Resistor
B. Transistor
C. Indicator lamp
D. Connector
Figure T1

## Slide 63: T6C03
What is component 2 in figure T-1?
A. Resistor
B. Transistor
C. Indicator lamp
D. Connector
Figure T1

## Slide 64: T6C04
What is component 3 in figure T-1?
A. Resistor
B. Transistor
C. Lamp
D. Ground symbol
Figure T1

## Slide 65: T6C04
What is component 3 in figure T-1?
A. Resistor
B. Transistor
C. Lamp
D. Ground symbol
Figure T1

## Slide 66: T6C05
What is component 4 in figure T-1?
A. Resistor
B. Transistor
C. Ground symbol
D. Battery
Figure T1

## Slide 67: T6C05
What is component 4 in figure T-1?
A. Resistor
B. Transistor
C. Ground symbol
D. Battery
Figure T1

## Slide 68: T6C06
What is component 6 in figure T-2?
A. Resistor
B. Capacitor
C. Regulator IC
D. Transistor
Figure T2

## Slide 69: T6C06
What is component 6 in figure T-2?
A. Resistor
B. Capacitor
C. Regulator IC
D. Transistor
Figure T2

## Slide 70: T6C07
What is component 8 in figure T-2?
A. Resistor
B. Inductor
C. Regulator IC
D. Light emitting diode
Figure T2

## Slide 71: T6C07
What is component 8 in figure T-2?
A. Resistor
B. Inductor
C. Regulator IC
D. Light emitting diode
Figure T2

## Slide 72: T6C08
What is component 9 in figure T-2?
A. Variable capacitor
B. Variable inductor
C. Variable resistor
D. Variable transformer
Figure T2

## Slide 73: T6C08
What is component 9 in figure T-2?
A. Variable capacitor
B. Variable inductor
C. Variable resistor
D. Variable transformer
Figure T2

## Slide 74: T6C09
What is component 4 in figure T-2?
A. Variable inductor
B. Double-pole switch
C. Potentiometer
D. Transformer
Figure T2

## Slide 75: T6C09
What is component 4 in figure T-2?
A. Variable inductor
B. Double-pole switch
C. Potentiometer
D. Transformer
Figure T2

## Slide 76: T6C10
What is component 3 in figure T-3?
A. Connector
B. Meter
C. Variable capacitor
D. Variable inductor
Figure T3

## Slide 77: T6C10
What is component 3 in figure T-3?
A. Connector
B. Meter
C. Variable capacitor
D. Variable inductor
Figure T3

## Slide 78: T6C11
What is component 4 in figure T-3?
A. Antenna
B. Transmitter
C. Dummy load
D. Ground
Figure T3

## Slide 79: T6C11
What is component 4 in figure T-3?
A. Antenna
B. Transmitter
C. Dummy load
D. Ground
Figure T3

## Slide 80: T6C12
Which of the following is accurately represented in electrical schematics?
A. Wire lengths
B. Physical appearance of components
C. Component connections
D. All these choices are correct

## Slide 81: T6C12
Which of the following is accurately represented in electrical schematics?
A. Wire lengths
B. Physical appearance of components
C. Component connections
D. All these choices are correct

## Slide 82
T6D - Component functions: rectifiers, relays, voltage regulators, meters, indicators, integrated circuits, transformers; Resonant circuit; Shielding
#22 of 35

## Slide 83: T6D01
Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier
C. Amplifier
D. Reflector

## Slide 84: T6D01
Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier
C. Amplifier
D. Reflector
A standard diode is also called a Rectifier.

## Slide 85: T6D02
Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier
C. Amplifier
D. Reflector

## Slide 86: T6D02
Which of the following devices or circuits changes an alternating current into a varying direct current signal?
A. Transformer
B. Rectifier (is the true correct answer)
C. Amplifier
D. Reflector
This is a wrong answer but if not updated by your test date you must answer Transformer to score a correct answer.

## Slide 87: T6D03
Which of the following is a reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other signals

## Slide 88: T6D03
Which of the following is a reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other signals

## Slide 89: T6D04
Which of the following displays an electrical quantity as a numeric value?
A. Potentiometer
B. Transistor
C. Meter
D. Relay

## Slide 90: T6D04
Which of the following displays an electrical quantity as a numeric value?
A. Potentiometer
B. Transistor
C. Meter
D. Relay

## Slide 91: T6D05
What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter

## Slide 92: T6D05
What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter

## Slide 93: T6D06
What component changes 120 V AC power to a lower AC voltage for other uses?
A. Variable capacitor
B. Transformer
C. Transistor
D. Diode

## Slide 94: T6D06
What component changes 120 V AC power to a lower AC voltage for other uses?
A. Variable capacitor
B. Transformer
C. Transistor
D. Diode

## Slide 95: T6D07
Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor

## Slide 96: T6D07
Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor

## Slide 97: T6D08
Which of the following is combined with an inductor to make a resonant circuit?
A. Resistor
B. Zener diode
C. Potentiometer
D. Capacitor

## Slide 98: T6D08
Which of the following is combined with an inductor to make a resonant circuit?
A. Resistor
B. Zener diode
C. Potentiometer
D. Capacitor

## Slide 99: T6D09
What is the name of a device that combines several semiconductors and other components into one package?
A. Transducer
B. Multi-pole relay
C. Integrated circuit
D. Transformer

## Slide 100: T6D09
What is the name of a device that combines several semiconductors and other components into one package?
A. Transducer
B. Multi-pole relay
C. Integrated circuit
D. Transformer

## Slide 101: T6D10
What is the function of component 2 in figure T-1?
A. Give off light when current flows through it
B. Supply electrical energy
C. Control the flow of current
D. Convert electrical energy into radio waves
Figure T1

## Slide 102: T6D10
What is the function of component 2 in figure T-1?
A. Give off light when current flows through it
B. Supply electrical energy
C. Control the flow of current
D. Convert electrical energy into radio waves
Figure T1

## Slide 103: T6D11
Which of the following is a resonant or tuned circuit?
A. An inductor and a capacitor in series or parallel
B. A linear voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high-fidelity audio

## Slide 104: T6D11
Which of the following is a resonant or tuned circuit?
A. An inductor and a capacitor in series or parallel
B. A linear voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high-fidelity audio

## Slide 105
End of Sub-element 6
(62% Complete)
Proceed to Sub-element 7 when ready