## Slide 1: Hi-Landers Ham Class
Instructed by Rich Bugarin W6EC

## Slide 2: Sub-element 7 of 10

## Slide 3
Ham Radio Technician Class Exam preparation Power Point created by Rich Bugarin W6EC.
Effective July 1, 2022 and is valid until June 30, 2026.
Please send suggested changes to this presentation to:
w6ec@thebugarins.com

## Slide 4: Study Hints
I suggest you read each question and only the correct answer. Read through the complete question pool at least three times before you attempt taking a practice exams. For higher impact and better results read the correct answer first then the question and again the correct answer.
The key to passing the exam is to get the most questions correct using the above method the correct response will often jump out at you on test day even if you don’t remember the question.

## Slide 5: Text Color
Black: Original/Official questions and information in original format (unaltered).
Red: Original information text color simply changed to highlight subject.
Blue: Notes and information added by Rich (W6EC).

## Slide 6
SUBELEMENT T7 – PRACTICAL CIRCUITS
[4 Exam Questions - 4 Groups]

## Slide 7
T7A – Station equipment: receivers, transceivers, transmitter amplifiers, receive amplifiers, transverters; Basic radio circuit concepts and terminology: sensitivity, selectivity, mixers, oscillators, PTT, modulation
#23 of 35

## Slide 8: T7A01
Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion

## Slide 9: T7A01
Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion

## Slide 10: T7A02
What is a transceiver?
A. A device that combines a receiver and transmitter
B. A device for matching feed line impedance to 50 ohms
C. A device for automatically sending and decoding Morse code
D. A device for converting receiver and transmitter frequencies to another band

## Slide 11: T7A02
What is a transceiver?
A. A device that combines a receiver and transmitter
B. A device for matching feed line impedance to 50 ohms
C. A device for automatically sending and decoding Morse code
D. A device for converting receiver and transmitter frequencies to another band

## Slide 12: T7A03
Which of the following is used to convert a signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier

## Slide 13: T7A03
Which of the following is used to convert a signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier

## Slide 14: T7A04
Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic distortion

## Slide 15: T7A04
Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic distortion

## Slide 16: T7A05
What is the name of a circuit that generates a signal at a specific frequency?
A. Reactance modulator
B. Phase modulator
C. Low-pass filter
D. Oscillator

## Slide 17: T7A05
What is the name of a circuit that generates a signal at a specific frequency?
A. Reactance modulator
B. Phase modulator
C. Low-pass filter
D. Oscillator

## Slide 18: T7A06
What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter

## Slide 19: T7A06
What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter
AKA cross band repeater

## Slide 20: T7A07
What is the function of a transceiver’s PTT input?
A. Input for a key used to send CW
B. Switches transceiver from receive to transmit when grounded
C. Provides a transmit tuning tone when grounded
D. Input for a preamplifier tuning tone

## Slide 21: T7A07
What is the function of a transceiver’s PTT input?
A. Input for a key used to send CW
B. Switches transceiver from receive to transmit when grounded
C. Provides a transmit tuning tone when grounded
D. Input for a preamplifier tuning tone

## Slide 22: T7A08
Which of the following describes combining speech with an RF carrier signal?
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering

## Slide 23: T7A08
Which of the following describes combining speech with an RF carrier signal?
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering

## Slide 24: T7A09
What is the function of the SSB/CW-FM switch on a VHF power amplifier?
A. Change the mode of the transmitted signal
B. Set the amplifier for proper operation in the selected mode
C. Change the frequency range of the amplifier to operate in the proper segment of the band
D. Reduce the received signal noise

## Slide 25: T7A09
What is the function of the SSB/CW-FM switch on a VHF power amplifier?
A. Change the mode of the transmitted signal
B. Set the amplifier for proper operation in the selected mode
C. Change the frequency range of the amplifier to operate in the proper segment of the band
D. Reduce the received signal noise

## Slide 26: T7A10
What device increases the transmitted output power from a transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All these choices are correct

## Slide 27: T7A10
What device increases the transmitted output power from a transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All these choices are correct
CB radio calls a power amp a linier amplifier

## Slide 28: T7A11
Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter power amplifier
C. Between the transmitter and the antenna tuner
D. At the output of the receiver audio amplifier

## Slide 29: T7A11
Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter power amplifier
C. Between the transmitter and the antenna tuner
D. At the output of the receiver audio amplifier

## Slide 30
T7B – Symptoms, causes, and cures of common transmitter and receiver problems: overload and overdrive, distortion, interference and consumer electronics, RF feedback
#24 of 35

## Slide 31: T7B01
What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone

## Slide 32: T7B01
What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone

## Slide 33: T7B02
What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low

## Slide 34: T7B02
What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low

## Slide 35: T7B03
Which of the following can cause radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All these choices are correct
Notes: all

## Slide 36: T7B03
Which of the following can cause radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All these choices are correct
Notes: all

## Slide 37: T7B04
Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke

## Slide 38: T7B04
Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke

## Slide 39: T7B05
How can fundamental overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode

## Slide 40: T7B05
How can fundamental overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode

## Slide 41: T7B06
Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
D. All these choices are correct

## Slide 42: T7B06
Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
D. All these choices are correct

## Slide 43: T7B07
Which of the following can reduce overload of a VHF transceiver by a nearby commercial FM station?
A. Installing an RF preamplifier
B. Using double-shielded coaxial cable
C. Installing bypass capacitors on the microphone cable
D. Installing a band-reject filter
Notes: all

## Slide 44: T7B07
Which of the following can reduce overload of a VHF transceiver by a nearby commercial FM station?
A. Installing an RF preamplifier
B. Using double-shielded coaxial cable
C. Installing bypass capacitors on the microphone cable
D. Installing a band-reject filter
Notes: all

## Slide 45: T7B08
What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor that FCC rules prohibit the use of devices that cause interference
C. Make sure your station meets the standards of good amateur practice
D. All these choices are correct
Notes: all

## Slide 46: T7B08
What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor that FCC rules prohibit the use of devices that cause interference
C. Make sure your station meets the standards of good amateur practice
D. All these choices are correct
Notes: all

## Slide 47: T7B09
What should be the first step to resolve non-fiber optic cable TV interference caused by your amateur radio transmission?
A. Add a low-pass filter to the TV antenna input
B. Add a high-pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV feed line coaxial connectors are installed properly

## Slide 48: T7B09
What should be the first step to resolve non-fiber optic cable TV interference caused by your amateur radio transmission?
A. Add a low-pass filter to the TV antenna input
B. Add a high-pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV feed line coaxial connectors are installed properly

## Slide 49: T7B10
What might be a problem if you receive a report that your audio signal through an FM repeater is distorted or unintelligible?
A. Your transmitter is slightly off frequency
B. Your batteries are running low
C. You are in a bad location
D. All these choices are correct
Notes: all

## Slide 50: T7B10
What might be a problem if you receive a report that your audio signal through an FM repeater is distorted or unintelligible?
A. Your transmitter is slightly off frequency
B. Your batteries are running low
C. You are in a bad location
D. All these choices are correct
Notes: all

## Slide 51: T7B11
What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible voice transmissions
D. Frequent blowing of power supply fuses

## Slide 52: T7B11
What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible voice transmissions
D. Frequent blowing of power supply fuses

## Slide 53
T7C – Antenna and transmission line measurements and troubleshooting: measuring SWR, effects of high SWR, causes of feed line failures; Basic coaxial cable characteristics; Use of dummy loads when testing
#25 of 35

## Slide 54: T7C01
What is the primary purpose of a dummy load?
A. To prevent transmitting signals over the air when making tests
B. To prevent over-modulation of a transmitter
C. To improve the efficiency of an antenna
D. To improve the signal-to-noise ratio of a receiver

## Slide 55: T7C01
What is the primary purpose of a dummy load?
A. To prevent transmitting signals over the air when making tests
B. To prevent over-modulation of a transmitter
C. To improve the efficiency of an antenna
D. To improve the signal-to-noise ratio of a receiver

## Slide 56: T7C02
Which of the following is used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter

## Slide 57: T7C02
Which of the following is used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter

## Slide 58: T7C03
What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor mounted on a heat sink
C. A low-voltage power supply and a DC relay
D. A 50-ohm reactance used to terminate a transmission line

## Slide 59: T7C03
What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor mounted on a heat sink
C. A low-voltage power supply and a DC relay
D. A 50-ohm reactance used to terminate a transmission line

## Slide 60: T7C04
What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 50:50
B. Zero
C. 1:1
D. Full Scale

## Slide 61: T7C04
What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 50:50
B. Zero
C. 1:1
D. Full Scale

## Slide 62: T7C05
Why do most solid-state transmitters reduce output power as SWR increases beyond a certain level?
A. To protect the output amplifier transistors
B. To comply with FCC rules on spectral purity
C. Because power supplies cannot supply enough current at high SWR
D. To lower the SWR on the transmission line

## Slide 63: T7C05
Why do most solid-state transmitters reduce output power as SWR increases beyond a certain level?
A. To protect the output amplifier transistors
B. To comply with FCC rules on spectral purity
C. Because power supplies cannot supply enough current at high SWR
D. To lower the SWR on the transmission line

## Slide 64: T7C06
What does an SWR reading of 4:1 indicate?
A. Loss of -4 dB
B. Good impedance match
C. Gain of +4 dB
D. Impedance mismatch

## Slide 65: T7C06
What does an SWR reading of 4:1 indicate?
A. Loss of -4 dB
B. Good impedance match
C. Gain of +4 dB
D. Impedance mismatch

## Slide 66: T7C07
What happens to power lost in a feed line?
A. It increases the SWR
B. It is radiated as harmonics
C. It is converted into heat
D. It distorts the signal

## Slide 67: T7C07
What happens to power lost in a feed line?
A. It increases the SWR
B. It is radiated as harmonics
C. It is converted into heat
D. It distorts the signal

## Slide 68: T7C08
Which instrument can be used to determine SWR?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter

## Slide 69: T7C08
Which instrument can be used to determine SWR?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter

## Slide 70: T7C09
Which of the following causes failure of coaxial cables?
A. Moisture contamination
B. Solder flux contamination
C. Rapid fluctuation in transmitter output power
D. Operation at 100% duty cycle for an extended period

## Slide 71: T7C09
Which of the following causes failure of coaxial cables?
A. Moisture contamination
B. Solder flux contamination
C. Rapid fluctuation in transmitter output power
D. Operation at 100% duty cycle for an extended period

## Slide 72: T7C10
Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable

## Slide 73: T7C10
Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable

## Slide 74: T7C11
What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent moisture in the cable
D. It cannot be used at below freezing temperatures

## Slide 75: T7C11
What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent moisture in the cable
D. It cannot be used at below freezing temperatures

## Slide 76
T7D – Using basic test instruments: voltmeter, ammeter, and ohmmeter; Soldering
#26 of 35

## Slide 77: T7D01
Which instrument would you use to measure electric potential?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter

## Slide 78: T7D01
Which instrument would you use to measure electric potential?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter
E = Electro Motive Force Measured in Volts = V

## Slide 79: T7D02
How is a voltmeter connected to a component to measure applied voltage?
A. In series
B. In parallel
C. In quadrature
D. In phase

## Slide 80: T7D02
How is a voltmeter connected to a component to measure applied voltage?
A. In series
B. In parallel
C. In quadrature
D. In phase
V

## Slide 81: T7D03
When configured to measure current, how is a multimeter connected to a component?
A. In series
B. In parallel
C. In quadrature
D. In phase

## Slide 82: T7D03
When configured to measure current, how is a multimeter connected to a component?
A. In series
B. In parallel
C. In quadrature
D. In phase
A

## Slide 83: T7D04
Which instrument is used to measure electric current?
A. An ohmmeter
B. An electrometer
C. A voltmeter
D. An ammeter

## Slide 84: T7D04
Which instrument is used to measure electric current?
A. An ohmmeter
B. An electrometer
C. A voltmeter
D. An ammeter
A

## Slide 85: T7D05
T7D05 Question Removed (section not renumbered)

## Slide 86: T7D06
Which of the following can damage a multimeter?
A. Attempting to measure resistance using the voltage setting
B. Failing to connect one of the probes to ground
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly

## Slide 87: T7D06
Which of the following can damage a multimeter?
A. Attempting to measure resistance using the voltage setting
B. Failing to connect one of the probes to ground
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly

## Slide 88: T7D07
Which of the following measurements are made using a multimeter?
A. Signal strength and noise
B. Impedance and reactance
C. Voltage and resistance
D. All these choices are correct

## Slide 89: T7D07
Which of the following measurements are made using a multimeter?
A. Signal strength and noise
B. Impedance and reactance
C. Voltage and resistance
D. All these choices are correct

## Slide 90: T7D08
Which of the following types of solder should not be used for radio and electronic applications?
A. Acid-core solder
B. Lead-tin solder
C. Rosin-core solder
D. Tin-copper solder

## Slide 91: T7D08
Which of the following types of solder should not be used for radio and electronic applications?
A. Acid-core solder
B. Lead-tin solder
C. Rosin-core solder
D. Tin-copper solder

## Slide 92: T7D09
What is the characteristic appearance of a cold tin-lead solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A rough or lumpy surface
D. Excessive solder

## Slide 93: T7D09
What is the characteristic appearance of a cold tin-lead solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A rough or lumpy surface
D. Excessive solder

## Slide 94: T7D10
What reading indicates that an ohmmeter is connected across a large, discharged capacitor?
A. Increasing resistance with time
B. Decreasing resistance with time
C. Steady full-scale reading
D. Alternating between open and short circuit

## Slide 95: T7D10
What reading indicates that an ohmmeter is connected across a large, discharged capacitor?
A. Increasing resistance with time
B. Decreasing resistance with time
C. Steady full-scale reading
D. Alternating between open and short circuit

## Slide 96: T7D11
Which of the following precautions should be taken when measuring in-circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency

## Slide 97: T7D11
Which of the following precautions should be taken when measuring in-circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency

## Slide 98
End of Sub-element 7
(74% completed)
Proceed to Sub-element 8 when ready