## Slide 1: Hi-Landers Ham Class
Instructed by Rich Bugarin W6EC

## Slide 2: Sub-element 8 of 10

## Slide 3
Ham Radio Technician Class Exam preparation Power Point created by Rich Bugarin W6EC.
Effective July 1, 2022 and is valid until June 30, 2026.
Please send suggested changes to this presentation to:
w6ec@thebugarins.com

## Slide 4: Study Hints
I suggest you read each question and only the correct answer. Read through the complete question pool at least three times before you attempt taking a practice exams. For higher impact and better results read the correct answer first then the question and again the correct answer.
The key to passing the exam is to get the most questions correct using the above method the correct response will often jump out at you on test day even if you don’t remember the question.

## Slide 5: Text Color
Black: Original/Official questions and information in original format (unaltered).
Red: Original information text color simply changed to highlight subject.
Blue: Notes and information added by Rich (W6EC).

## Slide 6
SUBELEMENT T8 – SIGNALS AND EMISSIONS
[4 Exam Questions - 4 Groups]

## Slide 7
T8A – Basic characteristics of FM and SSB; Bandwidth of various modulation modes: CW, SSB, FM, fast-scan TV; Choice of emission type: selection of USB vs LSB, use of SSB for weak signal work, use of FM for VHF packet and repeaters
#27 of 35

## Slide 8: T8A01
Which of the following is a form of amplitude modulation?
A. Spread spectrum
B. Packet radio
C. Single sideband
D. Phase shift keying (PSK)

## Slide 9: T8A01
Which of the following is a form of amplitude modulation?
A. Spread spectrum
B. Packet radio
C. Single sideband
D. Phase shift keying (PSK)

## Slide 10: T8A02
What type of modulation is commonly used for VHF packet radio transmissions?
A. FM or PM
B. SSB
C. AM
D. PSK

## Slide 11: T8A02
What type of modulation is commonly used for VHF packet radio transmissions?
A. FM or PM
B. SSB
C. AM
D. PSK

## Slide 12: T8A03
Which type of voice mode is often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM

## Slide 13: T8A03
Which type of voice mode is often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM

## Slide 14: T8A04
Which type of modulation is commonly used for VHF and UHF voice repeaters?
A. AM
B. SSB
C. PSK
D. FM or PM

## Slide 15: T8A04
Which type of modulation is commonly used for VHF and UHF voice repeaters?
A. AM
B. SSB
C. PSK
D. FM or PM

## Slide 16: T8A05
Which of the following types of signal has the narrowest bandwidth?
A. FM voice
B. SSB voice
C. CW
D. Slow-scan TV

## Slide 17: T8A05
Which of the following types of signal has the narrowest bandwidth?
A. FM voice
B. SSB voice
C. CW
D. Slow-scan TV

## Slide 18: T8A06
Which sideband is normally used for 10 meter HF, VHF, and UHF single-sideband communications?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Inverted sideband

## Slide 19: T8A06
Which sideband is normally used for 10 meter HF, VHF, and UHF single-sideband communications?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Inverted sideband

## Slide 20: T8A07
What is a characteristic of single sideband (SSB) compared to FM?
A. SSB signals are easier to tune in correctly
B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
D. All these choices are correct

## Slide 21: T8A07
What is a characteristic of single sideband (SSB) compared to FM?
A. SSB signals are easier to tune in correctly
B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
D. All these choices are correct

## Slide 22: T8A08
What is the approximate bandwidth of a typical single sideband (SSB) voice signal?
A. 1 kHz
B. 3 kHz
C. 6 kHz
D. 15 kHz

## Slide 23: T8A08
What is the approximate bandwidth of a typical single sideband (SSB) voice signal?
A. 1 kHz
B. 3 kHz
C. 6 kHz
D. 15 kHz

## Slide 24: T8A09
What is the approximate bandwidth of a VHF repeater FM voice signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz

## Slide 25: T8A09
What is the approximate bandwidth of a VHF repeater FM voice signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz
VHF ham (2 Meter) uses narrow spacing of 12.5 KHz

## Slide 26: T8A10
What is the approximate bandwidth of AM fast-scan TV transmissions?
A. More than 10 MHz
B. About 6 MHz
C. About 3 MHz
D. About 1 MHz

## Slide 27: T8A10
What is the approximate bandwidth of AM fast-scan TV transmissions?
A. More than 10 MHz
B. About 6 MHz
C. About 3 MHz
D. About 1 MHz

## Slide 28: T8A11
What is the approximate bandwidth required to transmit a CW signal?
A. 2.4 kHz
B. 150 Hz
C. 1000 Hz
D. 15 kHz

## Slide 29: T8A11
What is the approximate bandwidth required to transmit a CW signal?
A. 2.4 kHz
B. 150 Hz
C. 1000 Hz
D. 15 kHz
CW uses the least bandwidth of all transmission modes so pick small

## Slide 30: T8A12
Which of the following is a disadvantage of FM compared with single sideband?
A. Voice quality is poorer
B. Only one signal can be received at a time
C. FM signals are harder to tune
D. All these choices are correct

## Slide 31: T8A12
Which of the following is a disadvantage of FM compared with single sideband?
A. Voice quality is poorer
B. Only one signal can be received at a time
C. FM signals are harder to tune
D. All these choices are correct

## Slide 32
T8B - Amateur satellite operation: Doppler shift, basic orbits, operating protocols, modulation mode selection, transmitter power considerations, telemetry and telecommand, satellite tracking programs, beacons, uplink and downlink mode definitions, spin fading, definition of “LEO”, setting uplink power
#28 of 35

## Slide 33: T8B01
What telemetry information is typically transmitted by satellite beacons?
A. The signal strength of received signals
B. Time of day accurate to plus or minus 1/10 second
C. Health and status of the satellite
D. All these choices are correct

## Slide 34: T8B01
What telemetry information is typically transmitted by satellite beacons?
A. The signal strength of received signals
B. Time of day accurate to plus or minus 1/10 second
C. Health and status of the satellite
D. All these choices are correct

## Slide 35: T8B02
What is the impact of using excessive effective radiated power on a satellite uplink?
A. Possibility of commanding the satellite to an improper mode
B. Blocking access by other users
C. Overloading the satellite batteries
D. Possibility of rebooting the satellite control computer

## Slide 36: T8B02
What is the impact of using excessive effective radiated power on a satellite uplink?
A. Possibility of commanding the satellite to an improper mode
B. Blocking access by other users
C. Overloading the satellite batteries
D. Possibility of rebooting the satellite control computer

## Slide 37: T8B03
Which of the following are provided by satellite tracking programs?
A. Maps showing the real-time position of the satellite track over Earth
B. The time, azimuth, and elevation of the start, maximum altitude, and end of a pass
C. The apparent frequency of the satellite transmission, including effects of Doppler shift
D. All these choices are correct

## Slide 38: T8B03
Which of the following are provided by satellite tracking programs?
A. Maps showing the real-time position of the satellite track over Earth
B. The time, azimuth, and elevation of the start, maximum altitude, and end of a pass
C. The apparent frequency of the satellite transmission, including effects of Doppler shift
D. All these choices are correct

## Slide 39: T8B04
What mode of transmission is commonly used by amateur radio satellites?
A. SSB
B. FM
C. CW/data
D. All these choices are correct

## Slide 40: T8B04
What mode of transmission is commonly used by amateur radio satellites?
A. SSB
B. FM
C. CW/data
D. All these choices are correct

## Slide 41: T8B05
What is a satellite beacon?
A. The primary transmit antenna on the satellite
B. An indicator light that shows where to point your antenna
C. A reflective surface on the satellite
D. A transmission from a satellite that contains status information

## Slide 42: T8B05
What is a satellite beacon?
A. The primary transmit antenna on the satellite
B. An indicator light that shows where to point your antenna
C. A reflective surface on the satellite
D. A transmission from a satellite that contains status information

## Slide 43: T8B06
Which of the following are inputs to a satellite tracking program?
A. The satellite transmitted power
B. The Keplerian elements
C. The last observed time of zero Doppler shift
D. All these choices are correct

## Slide 44: T8B06
Which of the following are inputs to a satellite tracking program?
A. The satellite transmitted power
B. The Keplerian elements
C. The last observed time of zero Doppler shift
D. All these choices are correct

## Slide 45: T8B07
What is Doppler shift in reference to satellite communications?
A. A change in the satellite orbit
B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative motion between the satellite and Earth station
D. A special digital communications mode for some satellites

## Slide 46: T8B07
What is Doppler shift in reference to satellite communications?
A. A change in the satellite orbit
B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative motion between the satellite and Earth station
D. A special digital communications mode for some satellites

## Slide 47: T8B08
What is meant by the statement that a satellite is operating in U/V mode?
A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
B. The satellite uplink is in the 70 centimeter band and the downlink is in the 2 meter band
C. The satellite operates using ultraviolet frequencies
D. The satellite frequencies are usually variable

## Slide 48: T8B08
What is meant by the statement that a satellite is operating in U/V mode?
A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
B. The satellite uplink is in the 70 centimeter band and the downlink is in the 2 meter band
C. The satellite operates using ultraviolet frequencies
D. The satellite frequencies are usually variable

## Slide 49: T8B09
What causes spin fading of satellite signals?
A. Circular polarized noise interference radiated from the sun
B. Rotation of the satellite and its antennas
C. Doppler shift of the received signal
D. Interfering signals within the satellite uplink band

## Slide 50: T8B09
What causes spin fading of satellite signals?
A. Circular polarized noise interference radiated from the sun
B. Rotation of the satellite and its antennas
C. Doppler shift of the received signal
D. Interfering signals within the satellite uplink band

## Slide 51: T8B10
What is a LEO satellite?
A. A sun synchronous satellite
B. A highly elliptical orbit satellite
C. A satellite in low energy operation mode
D. A satellite in low earth orbit

## Slide 52: T8B10
What is a LEO satellite?
A. A sun synchronous satellite
B. A highly elliptical orbit satellite
C. A satellite in low energy operation mode
D. A satellite in low earth orbit

## Slide 53: T8B11
Who may receive telemetry from a space station?
A. Anyone
B. A licensed radio amateur with a transmitter equipped for interrogating the satellite
C. A licensed radio amateur who has been certified by the protocol developer
D. A licensed radio amateur who has registered for an access code from AMSAT

## Slide 54: T8B11
Who may receive telemetry from a space station?
A. Anyone
B. A licensed radio amateur with a transmitter equipped for interrogating the satellite
C. A licensed radio amateur who has been certified by the protocol developer
D. A licensed radio amateur who has registered for an access code from AMSAT

## Slide 55: T8B12
Which of the following is a way to determine whether your satellite uplink power is neither too low nor too high?
A. Check your signal strength report in the telemetry data
B. Listen for distortion on your downlink signal
C. Your signal strength on the downlink should be about the same as the beacon
D. All these choices are correct

## Slide 56: T8B12
Which of the following is a way to determine whether your satellite uplink power is neither too low nor too high?
A. Check your signal strength report in the telemetry data
B. Listen for distortion on your downlink signal
C. Your signal strength on the downlink should be about the same as the beacon
D. All these choices are correct

## Slide 57
T8C – Operating activities: radio direction finding, contests, linking over the internet, exchanging grid locators
#29 of 35

## Slide 58: T8C01
Which of the following methods is used to locate sources of noise interference or jamming?
A. Echolocation
B. Doppler radar
C. Radio direction finding
D. Phase locking

## Slide 59: T8C01
Which of the following methods is used to locate sources of noise interference or jamming?
A. Echolocation
B. Doppler radar
C. Radio direction finding
D. Phase locking

## Slide 60: T8C02
Which of these items would be useful for a hidden transmitter hunt?
A. Calibrated SWR meter
B. A directional antenna
C. A calibrated noise bridge
D. All these choices are correct

## Slide 61: T8C02
Which of these items would be useful for a hidden transmitter hunt?
A. Calibrated SWR meter
B. A directional antenna
C. A calibrated noise bridge
D. All these choices are correct

## Slide 62: T8C03
What operating activity involves contacting as many stations as possible during a specified period?
A. Simulated emergency exercises
B. Net operations
C. Public service events
D. Contesting

## Slide 63: T8C03
What operating activity involves contacting as many stations as possible during a specified period?
A. Simulated emergency exercises
B. Net operations
C. Public service events
D. Contesting

## Slide 64: T8C04
Which of the following is good procedure when contacting another station in a contest?
A. Sign only the last two letters of your call if there are many other stations calling
B. Contact the station twice to be sure that you are in his log
C. Send only the minimum information needed for proper identification and the contest exchange
D. All these choices are correct

## Slide 65: T8C04
Which of the following is good procedure when contacting another station in a contest?
A. Sign only the last two letters of your call if there are many other stations calling
B. Contact the station twice to be sure that you are in his log
C. Send only the minimum information needed for proper identification and the contest exchange
D. All these choices are correct

## Slide 66: T8C05
What is a grid locator?
A. A letter-number designator assigned to a geographic location
B. A letter-number designator assigned to an azimuth and elevation
C. An instrument for neutralizing a final amplifier
D. An instrument for radio direction finding

## Slide 67: T8C05
What is a grid locator?
A. A letter-number designator assigned to a geographic location
B. A letter-number designator assigned to an azimuth and elevation
C. An instrument for neutralizing a final amplifier
D. An instrument for radio direction finding

## Slide 68: T8C06
How is over the air access to IRLP nodes accomplished?
A. By obtaining a password that is sent via voice to the node
B. By using DTMF signals
C. By entering the proper internet password
D. By using CTCSS tone codes

## Slide 69: T8C06
How is over the air access to IRLP nodes accomplished?
A. By obtaining a password that is sent via voice to the node
B. By using DTMF signals
C. By entering the proper internet password
D. By using CTCSS tone codes

## Slide 70: T8C07
What is Voice Over Internet Protocol (VoIP)?
A. A set of rules specifying how to identify your station when linked over the internet to another station
B. A technique employed to “spot” DX stations via the internet
C. A technique for measuring the modulation quality of a transmitter using remote sites monitored via the internet
D. A method of delivering voice communications over the internet using digital techniques

## Slide 71: T8C07
What is Voice Over Internet Protocol (VoIP)?
A. A set of rules specifying how to identify your station when linked over the internet to another station
B. A technique employed to “spot” DX stations via the internet
C. A technique for measuring the modulation quality of a transmitter using remote sites monitored via the internet
D. A method of delivering voice communications over the internet using digital techniques

## Slide 72: T8C08
What is the Internet Radio Linking Project (IRLP)?
A. A technique to connect amateur radio systems, such as repeaters, via the internet using Voice Over Internet Protocol (VoIP)
B. A system for providing access to websites via amateur radio
C. A system for informing amateurs in real time of the frequency of active DX stations
D. A technique for measuring signal strength of an amateur transmitter via the internet

## Slide 73: T8C08
What is the Internet Radio Linking Project (IRLP)?
A. A technique to connect amateur radio systems, such as repeaters, via the internet using Voice Over Internet Protocol (VoIP)
B. A system for providing access to websites via amateur radio
C. A system for informing amateurs in real time of the frequency of active DX stations
D. A technique for measuring signal strength of an amateur transmitter via the internet

## Slide 74: T8C09
Which of the following protocols enables an amateur station to transmit through a repeater without using a radio to initiate the transmission?
A. IRLP
B. D-STAR
C. DMR
D. EchoLink

## Slide 75: T8C09
Which of the following protocols enables an amateur station to transmit through a repeater without using a radio to initiate the transmission?
A. IRLP
B. D-STAR
C. DMR
D. EchoLink

## Slide 76: T8C10
What is required before using the EchoLink system?
A. Complete the required EchoLink training
B. Purchase a license to use the EchoLink software
C. Register your call sign and provide proof of license
D. All these choices are correct

## Slide 77: T8C10
What is required before using the EchoLink system?
A. Complete the required EchoLink training
B. Purchase a license to use the EchoLink software
C. Register your call sign and provide proof of license
D. All these choices are correct

## Slide 78: T8C11
What is an amateur radio station that connects other amateur stations to the internet?
A. A gateway
B. A repeater
C. A digipeater
D. A beacon

## Slide 79: T8C11
What is an amateur radio station that connects other amateur stations to the internet?
A. A gateway
B. A repeater
C. A digipeater
D. A beacon

## Slide 80
T8D – Non-voice and digital communications: image signals and definition of NTSC, CW, packet radio, PSK, APRS, error detection and correction, amateur radio networking, Digital Mobile Radio, WSJT modes, Broadband-Hamnet
#30 of 35

## Slide 81: T8D01
Which of the following is a digital communications mode?
A. Packet radio
B. IEEE 802.11
C. FT8
D. All these choices are correct

## Slide 82: T8D01
Which of the following is a digital communications mode?
A. Packet radio
B. IEEE 802.11
C. FT8
D. All these choices are correct

## Slide 83: T8D02
What is a “talkgroup” on a DMR repeater?
A. A group of operators sharing common interests
B. A way for groups of users to share a channel at different times without hearing other users on the channel
C. A protocol that increases the signal-to-noise ratio when multiple repeaters are linked together
D. A net that meets at a specified time

## Slide 84: T8D02
What is a “talkgroup” on a DMR repeater?
A. A group of operators sharing common interests
B. A way for groups of users to share a channel at different times without hearing other users on the channel
C. A protocol that increases the signal-to-noise ratio when multiple repeaters are linked together
D. A net that meets at a specified time

## Slide 85: T8D03
What kind of data can be transmitted by APRS?
A. GPS position data
B. Text messages
C. Weather data
D. All these choices are correct

## Slide 86: T8D03
What kind of data can be transmitted by APRS?
A. GPS position data
B. Text messages
C. Weather data
D. All these choices are correct

## Slide 87: T8D04
What type of transmission is indicated by the term "NTSC?"
A. A Normal Transmission mode in Static Circuit
B. A special mode for satellite uplink
C. An analog fast-scan color TV signal
D. A frame compression scheme for TV signals

## Slide 88: T8D04
What type of transmission is indicated by the term "NTSC?"
A. A Normal Transmission mode in Static Circuit
B. A special mode for satellite uplink
C. An analog fast-scan color TV signal
D. A frame compression scheme for TV signals

## Slide 89: T8D05
Which of the following is an application of APRS?
A. Providing real-time tactical digital communications in conjunction with a map showing the locations of stations
B. Showing automatically the number of packets transmitted via PACTOR during a specific time interval
C. Providing voice over internet connection between repeaters
D. Providing information on the number of stations signed into a repeater

## Slide 90: T8D05
Which of the following is an application of APRS?
A. Providing real-time tactical digital communications in conjunction with a map showing the locations of stations
B. Showing automatically the number of packets transmitted via PACTOR during a specific time interval
C. Providing voice over internet connection between repeaters
D. Providing information on the number of stations signed into a repeater

## Slide 91: T8D06
What does the abbreviation "PSK" mean?
A. Pulse Shift Keying
B. Phase Shift Keying
C. Packet Short Keying
D. Phased Slide Keying

## Slide 92: T8D06
What does the abbreviation "PSK" mean?
A. Pulse Shift Keying
B. Phase Shift Keying
C. Packet Short Keying
D. Phased Slide Keying

## Slide 93: T8D07
Which of the following describes DMR?
A. A technique for time-multiplexing two digital voice signals on a single 12.5 kHz repeater channel
B. An automatic position tracking mode for FM mobiles communicating through repeaters
C. An automatic computer logging technique for hands-off logging when communicating while operating a vehicle
D. A digital technique for transmitting on two repeater inputs simultaneously for automatic error correction

## Slide 94: T8D07
Which of the following describes DMR?
A. A technique for time-multiplexing two digital voice signals on a single 12.5 kHz repeater channel
B. An automatic position tracking mode for FM mobiles communicating through repeaters
C. An automatic computer logging technique for hands-off logging when communicating while operating a vehicle
D. A digital technique for transmitting on two repeater inputs simultaneously for automatic error correction

## Slide 95: T8D08
Which of the following is included in packet radio transmissions?
A. A check sum that permits error detection
B. A header that contains the call sign of the station to which the information is being sent
C. Automatic repeat request in case of error
D. All these choices are correct

## Slide 96: T8D08
Which of the following is included in packet radio transmissions?
A. A check sum that permits error detection
B. A header that contains the call sign of the station to which the information is being sent
C. Automatic repeat request in case of error
D. All these choices are correct

## Slide 97: T8D09
What is CW?
A. A type of electromagnetic propagation
B. A digital mode used primarily on 2 meter FM
C. A technique for coil winding
D. Another name for a Morse code transmission

## Slide 98: T8D09
What is CW?
A. A type of electromagnetic propagation
B. A digital mode used primarily on 2 meter FM
C. A technique for coil winding
D. Another name for a Morse code transmission

## Slide 99: T8D10
Which of the following operating activities is supported by digital mode software in the WSJT-X software suite?
A. Earth-Moon-Earth
B. Weak signal propagation beacons
C. Meteor scatter
D. All these choices are correct

## Slide 100: T8D10
Which of the following operating activities is supported by digital mode software in the WSJT-X software suite?
A. Earth-Moon-Earth
B. Weak signal propagation beacons
C. Meteor scatter
D. All these choices are correct

## Slide 101: T8D11
What is an ARQ transmission system?
A. A special transmission format limited to video signals
B. A system used to encrypt command signals to an amateur radio satellite
C. An error correction method in which the receiving station detects errors and sends a request for retransmission
D. A method of compressing data using autonomous reiterative Q codes prior to final encoding

## Slide 102: T8D11
What is an ARQ transmission system?
A. A special transmission format limited to video signals
B. A system used to encrypt command signals to an amateur radio satellite
C. An error correction method in which the receiving station detects errors and sends a request for retransmission
D. A method of compressing data using autonomous reiterative Q codes prior to final encoding

## Slide 103: T8D12
Which of the following best describes an amateur radio mesh network?
A. An amateur-radio based data network using commercial Wi-Fi equipment with modified firmware
B. A wide-bandwidth digital voice mode employing DMR protocols
C. A satellite communications network using modified commercial satellite TV hardware
D. An internet linking protocol used to network repeaters

## Slide 104: T8D12
Which of the following best describes an amateur radio mesh network?
A. An amateur-radio based data network using commercial Wi-Fi equipment with modified firmware
B. A wide-bandwidth digital voice mode employing DMR protocols
C. A satellite communications network using modified commercial satellite TV hardware
D. An internet linking protocol used to network repeaters

## Slide 105: T8D13
What is FT8?
A. A wideband FM voice mode
B. A digital mode capable of low signal-to-noise operation
C. An eight channel multiplex mode for FM repeaters
D. A digital slow-scan TV mode with forward error correction and automatic color compensation

## Slide 106: T8D13
What is FT8?
A. A wideband FM voice mode
B. A digital mode capable of low signal-to-noise operation
C. An eight channel multiplex mode for FM repeaters
D. A digital slow-scan TV mode with forward error correction and automatic color compensation

## Slide 107
End of Sub-element 8
(85% complete)
Proceed to Sub-element 9 when ready